## Slide 1: EE359 – Lecture 2 Outline
Announcements
  1st HW posted, due next Friday at 4pm.
  Discussion section and TA OHs starts next week
  Will finalize makeup lecture schedule today
Review of Last Lecture
TX and RX Signal Models
Path Loss Models
  Free-space and 2-Ray Models
  General Ray Tracing
  Single-Slope Path Loss Exponent Model
  Empirical Models
  mmWave Models

## Slide 2: Makeup lecture options
Next Thursday
  Monday (1/13): 11:30-12:50pm w/lunch
  Tuesday (1/14): 3:00-4:20 or 4:30-5:50pm (+lecture 1:30-2:50)
  Wednesday (1/15): 9:00-10:20am or 11:30-12:50pm*
  Regular Time Thu 1:30-2:50pm with Tom giving lecture
  Friday (1/17): 9:00-10:20am* or 3:30-4:50pm
    Following Monday is MLK 3-day weekend
Thu 2/20 moved to Fri 2/21 from 3:30-4:50pm
  MT week, could do Fri 9am instead
Tue 2/4 moved to Wed 2/5 11:30-12:50pm w/lunch
Thu 3/5 moved to Wed 3/4 11:30-12:50pm w/lunch
  Could do Wed am or Friday 9am or 3:30 instead
Regular time
with Tom
*Pending availability

## Slide 3: Lecture 1 Review
Course Information
Wireless Vision
Technical Challenges
Current/Next-Gen Wireless Systems
Spectrum Regulation and Standards
Emerging Wireless Systems
Emerging systems can be covered in a bonus lecture

## Slide 4: Propagation Characteristics
Path Loss (includes average shadowing)
Shadowing (due to obstructions)
Multipath Fading
Pr/Pt
d=vt
Pr
Pt
d=vt
v
Very slow
Slow
Fast

## Slide 5: Path Loss Modeling
Maxwell’s equations
  Complex and impractical
Free space and 2-path models
  Too simple
Ray tracing models
  Requires site-specific information
Single-slope path loss exponent model
  Main characteristics: good for high-level analysis
Measurement-based and Standards Models
  Not accurate; used to assess different designs

## Slide 6: Free Space (LOS) Model
Path loss for unobstructed LOS path
Power falls off :
  Proportional to 1/d2
  Proportional to l2 (inversely proportional to f2)
    This is due to the effective aperture of the antenna
d=vt

## Slide 7: Two Ray Model
Path loss for one LOS path and 1 ground (or reflected) bounce
Ground bounce approximately cancels LOS path above critical distance
Power falls off
  Proportional to d2 (small d)
  Proportional to d4 (d>dc)
  Independent of l (fc)
    Two-path cancellation equivalent to 2-element array, i.e. the effective aperature of the receive antenna is changed.

## Slide 8: General Ray Tracing
Models signal components as particles
  Reflections
  Scattering
  Diffraction
Requires site geometry and dielectric properties
  Easier than Maxwell (geometry vs. differential eqns)
Computer packages often used
Reflections generally dominate
10-ray reflection model explored in HW

## Slide 9: Simplified Path Loss Model
Used when path loss dominated by reflections.
Most important parameter is the path loss exponent g, determined empirically.
r

## Slide 10: mmWave: What’s the big deal?
All existing commercial systems fit into a small fraction of the mmWave band

## Slide 11: mmWave Propagation (60-100GHz)
Channel models immature
  Based on measurements, few accurate analytical models
Path loss proportion to l2 (huge)
Also have oxygen and rain absorbtion
  l is on the order of a water molecule
mmWave systems will be short range or require “massive MIMO”
mmW
Massive
MIMO

## Slide 12: Empirical Channel Models (not covered in lecture, not on HW/exams)
Early cellular empirical models:
  Empirical path loss models for early cellular systems were based on extensive measurements.
  Okumura model: empirically based (site/freq specific), uses graphs
  Hata model: Analytical approximation to Okumura
  Cost 231 Model: extends Hata to higher freq. (2 GHz)
  Multi-slope model
  Walfish/Bertoni: extends Cost 231 to include diffraction
Current cellular models (LTE and 5G):
  Detailed path loss models for UE (3GPP TS 36.101) and base stations (3GPP TS 36.104) for different multipath delay spreads, user speeds and MIMO antenna correlations.
  The 5G model includes higher frequencies (up to 100 GHz).
WiFi channel models: TGn and TGac
  Indoor and outdoor path loss models with MIMO (4x4 & greater), 40 MHz channels (& greater), and different multipath delay spread.
Commonly used in cellular and WiFi system simulations

## Slide 13: Main Points
Path loss models simplify Maxwell’s equations
Models vary in complexity and accuracy
Power falloff with distance is proportional to d2 in free space, d4 in two path model
Main characteristics of path loss captured in single-slope exponent model Pr=PtK[dr/d]g
mmWave propagation models still immature
  Path loss large due to frequency, rain, and oxygen
Empirical models used in simulations