## Slide 1
Department of Electrical Engineering
University of Arkansas
ELEG 5693 Wireless Communications
Math Review
Dr. Jingxian Wu
Jingxian.wu@sonoma.edu

## Slide 2: OUTLINE
2
Signals and System (Fourier analysis)
Random variables and random process

## Slide 3: CONCEPT OF FREQUENCY
3
Frequency is the measurement of the number of times that a repeated event occurred in a unit time (1 second).
  Frequency measures how fast a signal can change within a unit period of
time (or the measurement of the rate of change).
  High frequency  the signal changes fast
In signal processing, frequency is defined based on sinusoid signal  number of cycles per second.
  Each sinusoid signal is uniquely associated with a single frequency based on its rate of change.
f = 0 Hz
f = 1 Hz
f = 3 Hz
1 second

## Slide 4: TIME DOMAIN SIGNAL
4
Sinusoid Signal
s(t)  Asin( 2ft  )
  f : frequency. in the unit of Hz (1/second)
  A : amplitude. maximum strength in signal, usually in unit of volts
   : phase. relative position in time
t : time. in the unit of second
T : period. Time for one cycle or one repetition, T=1/f.
 : Wavelength. Distance of the signal waveform propagated in one period T.
    vT , where v is the speed of the signal. In vacuum, it is the speed of light.
A

2f
T
0 second

## Slide 5: THEORY: FREQUENCY DOMAIN SIGNAL
5
Periodic signal can be written as the summation of a series of sinusoids (Fourier Series)
Each sinusoid component has a unique frequency
Each sinusoid component is called a “harmonic” of the original signal.
There is a one to one relationship between a signal and its Fourier series.
With Fourier series, we can represent the signal in the “Frequency Domain”

2
n1 n1
n n
a sin( 2
 
s(t)  1 c  
bn cos(2nfnt)
nf t) 
s(t)
Time Domain
n n
a2
 b2
n
2
2
a2
 b2
Frequency Domain

## Slide 6
6
FOURIER TRANSFORM
Let g(t) be a non-periodic deterministic signal, expressed as function of t. Its frequency domain representation, G(f) , can be obtained from Fourier transform.

Fourier transform
G( f )   g(t) exp( j2ft)dt

Inverse Fourier transform
g(t)   G( f ) exp( j2ft)dt
j2  1
exp( jx)  cos(x)  j sin( x)

## Slide 7: FOURIER TRANSFORM
7
Example 1:
Find the Fourier transform of g(t)  exp(t) , t > 0
Sol.

## Slide 8
8
FOURIER TRANSFORM
s(t)  et ,
1
1 j2f
S( f ) 
t  0
Time Domain
Frequency Domain
Fourier Transform

## Slide 9
9
UNIT IMPULSE FUNCTION
Unit impulse function (delta function)

  (t)dt  1,

 (t)x(t)   (t)x(0)


 (t) exp( j2 ft)dt 
 (t)  0,t  0
1
t
 (t)
1
f
F  (t)
 (0)  ,

## Slide 10
10
The output of the LTI system is the convolution of input x(t)
with the channel impulse response h(t)
 
y(t)  x(t)  h(t)   x(t  )h( )d   x( )h(t  )d
  Time domain convolution  frequency domain multiplication
X ( f )  Fx(t) H ( f )  F h(t) Y ( f )  F y(t)
LINEAR TIME INVARIANT (LTI) SYSTEM
h(t)
y(t)
Y ( f )  X ( f )  H ( f )
x(t)

## Slide 11
11
LTI
h(t)
Example:
x(t)
x(t)   (t)
y(t)
y(t)  ?
h(t)  exp(t), t  0
Method 1:
Method 2:

## Slide 12: CORRELATION
12
The cross correlation of two deterministic, complex-valued function a(t) and b(t) is defined as


ab
*
a(t)b (t  )dt
R ( ) 
The auto-correlation of one deterministic, complex-valued function a(t) is defined as


a
*
a(t)a (t  )dt
R ( ) 

## Slide 13
13
ENERGY
The energy of a signal s(t) is defined as


E 
s
s(t) 2 dt
If a signal has finite energy, the signal is called energy signal.
E.g. s(t)  exp(t), t  0
Es 
s
s
s(t)s* (t  0)dt  R (0)
s(t) 2 dt 
E 




Relationship between energy and auto-correlation function

## Slide 14: POWER
14
The power of a signal s(t) is defined as
If a signal has finite power, the signal is called power signal
For periodic signal with period T
– E.g.

T
s
T
0
s(t) 2 dt
P  1
s(t)  Asin( 2ft  )
Ps 

2
1
T / 2
T / 2
s
s(t) dt
T  T
P  lim

## Slide 15
15
PARSEVAL’S THEOREM & ESD

2
f1
2
S( f ) df
f
S( f ) 2 is called the energy spectrum density (ESD) of the signal
– ESD represents the energy distribution in the frequency domain.
e.g. ESD of
s(t)  exp(t), t  0
:The signal energy in the
frequency range of
1 2
[ f , f ]


 
E 
s
s(t) 2dt  S ( f ) 2 df
1
|1 j2f |2

## Slide 16: OUTLINE
16
Linear system theory (Fourier analysis) (Appendix A)
Random variables and random process (Appendix C)

## Slide 17: CUMLATIVE DISTRIBUTION FUNCTION (CDF)
18
Example 1: toss coin
FX (x)  P( X  x)
0,
x  0
0  x  1
P( X  0)  P( X  1)  1, x  1
X
F (x)   P( X  0)  0.5,



X
Example 2: pick 1 balls from 10 balls


F (x)  



x  0
0  x  1
1  x  2
x  2

## Slide 18: CONTINUOUS RV
19
RV X can take continuous values
– E.g.: X represents the average temperature
CDF
Probability density function (pdf)
FX (x)  P( X  x)
FX ()  0
FX () 1
X
f
(x)  dFX (x)
dx
(x)  FX (x  x)  FX (x)  P(x  X  x  x)
Interpretation: for small x ,
X
f
x x
f X (x)x  P(x  X  x  x)
or, the probability that the RV X is in the range of
(x, x  x)

## Slide 19
20
PDF AND CDF
Relationship between pdf and CDF
X
dF (x)
dx
f (x)  X
x
X
X
f ( y)dy

F (x) 


P( X  )  FX ()   f X ( y)dy  1
2
1
x
X
x
f ( y)dy
P(x2  X  x1 )  FX (x2 )  FX (x1 ) 


## Slide 20: CDF AND PDF
22
a b
cdf of uniform distribution
1/(b-a)
a b
pdf of uniform distribution
0
1

## Slide 21
23
EXPECTATION (MEAN)
Discrete-time RV
mX  E( X )   xi P( X  xi )
i
– Weighted sum
Continuous-time RV

mX  E( X )   yf X ( y)dy
Example: find the expectation (mean) of the uniform distribution
1
, a  x  b
X
f (x) 
b  a

## Slide 22
24
VARIANCE
Discrete RV

2
X
X
X
f ( y)dy
y  m

 2 =E ( X  m )2  
 

Continuous RV


2
2
2
X
i
P( X  x )
x  m
 i X i


 =E ( X  m ) 


 
2
2
2
X
 =E X  m
•
– Proof:

## Slide 23
26
GAUSSIAN DISTRIBUTION
The pdf of Gaussian distribution is




2
exp 
2
1
2 
(x  m)2 
f X (x) 
– The pdf is determined by two parameters:
m  EX 
  EX  mX 
2
mean
standard deviation
The sum of Gaussian RVs is still Gaussian distributed

## Slide 24
27
GAUSSIAN DISTRIBUTION
mean

## Slide 25
28
JOINT DISTRIBUTION
Consider two RVs, X, and, Y. The joint CDF of X and Y is
FX ,Y (x, y)  P( X  x,Y  y)
Joint pdf
xy
(x, y)  FX ,Y (x, y)
f
X ,Y
Given the joint pdf, we can find the marginal pdf of each RV



f (x, y)dy
X ,Y
X
f (x) 



f (x, y)dx
X ,Y
Y
f ( y) 
Independent
– If f X ,Y (x, y)  f X (x) fY ( y) , then X and Y are independent.

## Slide 26
30
CORRELATION
The correlation of two RVs X and Y is calculated as
EXY  
 
 
XY
 
xyf (x, y)dxdy
The covariance of two RVs X and Y is
EX  mX Y  mY   E[x]E[Y ]  mX mY
If EXY   E( X )E(Y ) , then X and Y are uncorrelated.
If X and Y are independent  they must be uncorrelated.

## Slide 27: CORRELATION
31
Example:
Are X, Y uncorrelated?
– Sol:

x  y,
f X ,Y (x, y)  
0  x  1,0  y  1 otherwise
0,

## Slide 28: RANDOM PROCESS
32
At each time instant, we have a RV
Random process X(t): an RV changes w.r.t. time
  X(t) is a function of time t
  At any time instant t0 , X (t0 ) is a random variable.
Each realization is called a sample function of the random process
mean: (ensemble average)
mX (t0 )  E[X (t0 )]
Time (ms)

## Slide 29
33
at time
, we have a RV
Then we have the joint distribution functions
t1
RANDOM PROCESS
Let X (t) be a random process,
at time t2 , we have another RV
X (t1 ) ;
X (t2 ) .
2
2
1 1
2
1
X (t ) X (t ) 1 2
X (t )  x , X t   x 
F (x , x )  P
1 2
1 2
(x , x )
X (t ) X (t ) 1 2
x x
F
f
X (t1 ) X (t2 ) 1 2
(x , x ) 

## Slide 30
34
at time
Then we can calculate the correlation of X (t1 )
and X (t2 ) :
t1
AUTO-CORRECTION FUNCTION (ACF)
Let X (t) be a random process,
at time t2 , we have another RV
, we have a RV X (t1 ) ;
X (t2 ) .
2
*
X (t )X t 
X 1 2 1
R (t ,t )  E 
RX (t1 , t2 )
is defined as the autocorrelation function of X(t)

## Slide 31
35
WIDE-SENSE STATIONARY (WSS)
A random process is wide-sense stationary (WSS) if the following two conditions are satisfied
mX (t)  E[ X (t)]  mX
1.
2.
mX (t)  EX (t) mx
RX (t1, t2 )  RX (t1  h, t2  h)  RX (t1  t2 )
The first condition states that the mean of the random process is independent of time.
The second condition states that the auto-correlation function is only
dependent on the time difference between the two RVs, and it’s independent
of the starting time.
E[ X (t1 ) X (t2 )]  EX (t1  h) X (t2  h)
  The autocorrelation function of WSS process is usually represented as
RX ( )

## Slide 32
36
POWER SPECTRUM DENSITY
The power spectrum density (PSD) of WSS random process is defined as the Fourier transform of the auto-correlation function of the process

SX ( f )   RX ( ) exp( j2f )d
Power spectrum density represents the power distribution in the frequency domain.
E.g.
 ( )
2
0
N
x
R ( ) 
2
2
0
0
N N
x
S ( f ) 


 ( )d 
f
SX  f 
N0/2
RX ( )
N0/2


## Slide 33
37
RANDOM PROCESS PASS THROUGH LTI
h(t)
y(t)
x(t)
X
Y
S ( f )  H ( f ) S ( f )
The relationship between PSD of y(t) and PSD of x(t)
2








 

h(t  )Ex( )d
h(t  )x( )d
Ey(t) E
If x(t) is a WSS random process, then y(t) is a WSS random process as well.
The relationship between mean of y(t) and mean of x(t)

## Slide 34
Department of Electrical Engineering
University of Arkansas
ELEG 5693 Wireless Communications
Introduction
Dr. Jingxian Wu
wuj@uark.edu

## Slide 35: OUTLINE
2
Background
Major modern wireless communication standards
Basic Concepts
Block diagrams of a wireless communication system

## Slide 36: BACKGROUND
3
Wireless Communications:
– Transmit information from transmitter to receiver through the
propagation of unguided electromagnetic waves (channel).
Transmitter
Channel
Receiver
Wireless communication: channel is wireless!
Wireless channel imposes numerous challenges.
This course:
  How to characterize the wireless channel?
  How to efficiently and accurately transmit signal over the wireless channel? (How to format signals based on the properties of wireless channel?)

## Slide 37: BACKGROUND: MILESTONES
4
1864. Maxwell predicted the existence of electromagnetic wave (radio wave).
1887 Hertz demonstrated the existence of radio wave.
1901 Marconi realized first across Atlantic wireless transmission (England to Canada)
1906 First radio broadcast (AM radio)
1946 First public mobile telephone systems
1981 First analog cellular system in Scandinavia.
  Prototype of current cellular systems.
  1983, Advanced Mobile Phone Service (AMPS) in North America.
2019 First 5th generation (5G) services launched in US and
China

## Slide 38: BACKGROUND: SPECTRUM
5
Radio Frequency (RF)
  1MHz to 1GHz (general classification, not absolute)
  100 MHz to 1GHz (more widely used definition)
  Applications: AM radio, FM radio, TV, some cellular telephone systems, etc.
Microwave
  1 GHz to 300 GHz (general)
  1 GHz to 100 GHz (more widely used)
  Most cellular telephone systems, wireless LAN, Satellite, etc.
Trends towards use of higher frequencies
  Maximum bandwidth  10% of carrier frequency
  More users and higher data rate
  More difficult to design  more $$

## Slide 39: BACKGROUND: EXAMPLES
6
Garage door opener
Remote control
Paging system
Cordless telephone system
Fixed microwave
  Point-to-point link for long distance telephone
  Most have been replaced by fiber optics.
Cellular telephone system
Wireless local area network (LAN)
Wireless sensor networks (WSN)
Vehicular Ad-hoc network (VANET)
Internet-of-Things (IoT)

## Slide 40: OUTLINE
7
Background
Major modern wireless communication standards
Basic Concepts
Block diagrams of a wireless communication system

## Slide 41: STANDARDS: MOBILE TELEPHONE SYSTEMS
8
1st generation: analog voice
  Example: Advanced Mobile Phone Service (AMPS)
2nd generation: digital voice and narrowband data
  Examples: GSM (T-Mobile, Cingular, AT&T, Verizon), D-AMPS (AT&T), IS-95 (Interim Standard-95) (Sprint)
  2.5 generation: EDGE, GPRS
3rd generation: digital voice and broadband data
  Examples: WCDMA (HSDPA), cdma2000 (EV-DO)
4th generation: broadband multimedia communication
  LTE (long term evolution)
  LTE advanced (true 4G)

## Slide 42: STANDARDS: MOBILE TELEPHONE SYSTEMS
5th generation: seamless wireless coverage everywhere
  Standard: IMT-2020 (International Mobile Telecommunication
2020)
    It specifies all the requirements for 5G
  3GPP develops the actual standards that meet all IMT-2020
requirements
    NR (new radio),
    NB-IoT (narrowband Internet-of-Things),
    LTE-M (Long term evolution – Machine type communications)
  Usage scenarios:
    Enhanced Mobile Broadband (eMBB)
    Ultra-Reliable Low-Latency Communications (URLLC)
    Massive Machine-Type Communications (mMTC)
9

## Slide 43: STANDARDS: MOBILE TELEPHONE SYSTEMS
10
AMPS
  Advanced Mobile Phone System
  1983, AT&T
  Analog voice (control information is digital)
Frequency Division Multiple Access (FDMA)
Available spectrum divided into channels
each user is assigned a channel
(c) The multiplexed channel
(b) Bandwidths raised in frequency
(a) The original
bandwidths

## Slide 44: STANDARDS: MOBILE TELEPHONE SYSTEMS
11
D-AMPS (IS-54/136)
  Digital AMPS
  Digital voice: analog voice is digitalized and compressed by vocoder before Tx
Time Division Multiple Access (TDMA)
  Time is divided into frame, frame divided into slots
  Each user is assigned one or more slots
  TDMA is usually on top of FDMA (30 KHz channel, 6 users per channel)

## Slide 45: STANDARDS: MOBILE TELEPHONE SYSTEMS
12
GSM (Global System for Mobile communication)
  The most widely used 2nd generation system
  Similar to D-AMPS, but with different format

## Slide 46: STANDARDS: MOBILE TELEPHONE SYSTEMS
13
IS-95 (Narrowband CDMA)
  Code Division Multiple Access
  All users Tx simultaneously using the same frequency and same time.
  Different codes are used to separate the signals from different users.
CDMA
  Each user is assigned a unique code
  The code is known at both transmitter (Tx) and receiver (Rx)
  All users Tx at the same frequency and time
  Receiver uses codes to pick up desired signals
  Also called spread spectrum
  (details will be discussed in Ch. 9)

## Slide 47: STANDARDS: MOBILE TELEPHONE SYSTEMS
14
WCDMA (Wideband CDMA)
  Also called UMTS (Universal Mobile Telephone System)
  Proposed by Ericsson, Standardized in 3GPP
  Will mainly be used in Europe
  Data: HSDPA (High Speed Downlink Packet Access, 1.8 Mbps-7.2 Mbps)
cdma2000
  Proposed by Qualcomm, Standardized in 3GPP2
  Will mainly be used in North America
  Data: 1xEV-DO (Evolution Data Optimization, 1x: one 1.25 MHz channel, up to 4.9 Mbps in the downlink)
Both standards use CDMA
  Only some detailed technical differences

## Slide 48: STANDARDS: MOBILE TELEPHONE SYSTEMS
4G: LTE (long term evolution)
  Standard finalized in 2008
  First LTE service in North America launched by Verizon in 2010.
  An upgrade of 3G UMTS
Some main features
  OFDMA (orthogonal frequency division multiple access) for downlink; FDMA for uplink
  Scalable carrier bandwidth: 1.4 MHz, 3 MHz, 5 MHz, 10 MHz,
15 MHz and 20 MHz
  Low latency: sub-5 ms latency for small packets in optimal conditions
  Peak download rate: 299.6 Mbps; Peak upload rate: 75.4 Mbps
  Cell size: tens of meters radius (femto and picocells) up to 100 km (62
miles) radius marcocells. (Typical radius 5 – 30 kms)
15

## Slide 49: STANDARDS: MOBILE TELEPHONE SYSTEMS
5G
  IMT 2020: issued in 2015, expected to be completed in 2020
  3GPP Release-15 completed in 2019, release-20 to be completed in 2020
16

## Slide 50: STANDARDS
17
5G usage scenarios
  Enhanced Mobile Broadband (eMBB)
  Ultra-Reliable Low-Latency Communications (URLLC)
  Massive Machine-Type Communications (mMTC)

## Slide 51: STANDARDS
5G requirements
18

## Slide 52: STANDARDS: WIRELSS LAN
19
IEEE 802.11 (WiFi)
– IEEE 802.11a (Oct. 1999)
  Operating at 5.8GHz, up to 54Mbps
  Orthogonal Frequency Division Multiplex (OFDM)
– IEEE 802.11b (Oct. 1999)
  Operating at 2.4GHz, up to 11Mbps
  Direct Sequence Spread Spectrum (DSSS, CDMA)
– IEEE 802.11g (Jun. 2003)
  Operating at 2.4GHz, up to 54Mbps
  OFDM
– IEEE 802.11n (2009)
  Operating at 2.4 GHz or 5.8 GHz, up to 540 Mbps
  Channel bandwidth up to 40 MHz
  MIMO (Multiple input multiple output, up to 4 x 4)
IEEE 802.11ac (2011 to present)
  Operating at 5.8 GHz, up to 1 Gbps for multi-station WLAN, upto 500 Mbps
for a single link
  Wider bandwidth (up to 160 MHz), MIMO (up to 8x8), multi-user MIMO, high density modulation (upto 256 QAM)
– IEEE 802.11ad (2014 to present)
  60 GHz carrier frequency, upto 7 Gbps (WiGig)

## Slide 53: OUTLINE
20
Background
Major modern wireless communication standards
Basic concepts
Block diagrams of a wireless communication system

## Slide 54: CONCEPTS
21
In most wireless communication systems, the wireless communication occurs between mobile station (MS) and base station (BS)
  MS: Cell phone, wireless laptop, wireless PDA, etc.
  BS: wireless access point, wireless router, etc.
Downlink
  Radio channel for transmission from BS to MS
  Also called forward link
Uplink
  Radio channel for transmission from MS to BS
  Also called reverse link

## Slide 55: CONCEPTS: SIMPLEX AND DUPLEX
22
Simplex
  Communication occurs only in one direction
  E.g. paging system
Half Duplex
  Tx can occur in either direction, but only one way at a time.
  E.g. Walki-Talki (police radio)
Full Duplex
  Tx can occur at both direction simultaneously
  E.g. Telephone.
  Two simplex  One Full Duplex

## Slide 56: CONCEPTS:FDD V.S TDD
23
Frequency Division Duplex (FDD)
– Two distinct frequencies are used for downlink and uplink.
Time Division Duplex (TDD)
  Two distinct sets of time slots at the same frequency are used for downlink and uplink
TDD  TDMA, FDD  FDMA
  TDMA or FDMA: multiple users use different time/frequency
  TDD or FDD: uplink and downlink (belonging to same user) use different time/frequency
  TDD can be used in FDMA, TDMA, and CDMA systems
  FDD can be used in FDMA, TDMA, and CDMA systems
  E.g. FDD and TDMA can be in one system.
e.g. AMPS: forward link: 824 ~ 849 MHz
reverse link: 869 ~ 894 MHz

## Slide 57: CONCEPTS: CELLUAR
24
Motivations
  Early mobile phone system uses a single high Tx tower to cover a
large spatial area (high tower, high power)
  Limited spectrum can only support a small number of users.
  How can we support simultaneous communications of practically
unlimited number of users?
Solution: cellular concept with frequency reuse
  Many Tx towers (base station)
  Each covers a certain area: cell
  Frequencies can be reused from area to area

## Slide 58: CONCEPTS: CELLULAR
25
Cellular Concept with Frequency Reuse
  The entire coverage area is divided into cells
  A base station (BS) in the center of each cell.
  Communication occurs between BS and Mobile Stations (MS) in cell.
  The same frequency (channels) can be reused by nearby cells 
Frequency Reuse
    But not by adjacent cells!Reduce co-channel interference (CCI).
      Hexagonal shape only for the
convenience of analysis
        Circle leaves gaps
      Actual cell “footprint” is amorphous
        No specific shape

## Slide 59: CONCEPTS: CELLULAR
26
Cluster
  Cluster: Group of N cells using complete set of available channels.
  Cells belonging to the same clusters use different frequencies
For hexagonal cells, the cluster size N must satisfy
  N = i^2 + i j + j^2 where i, j  1
  typical N values  3, 7, 12
    (i, j) = (1,1)  N = 1+1+1 = 3
    (i, j) = (1, 2)  N = 1+2+4 = 7
    (i, j) = (2, 2)  N = 4+4+4 = 12
    (i, j) = (2, 3)  N = 4+6+9 = 19
Cell radius R:
AMPS: 10 ~ 20 km
WCDMA: 1 ~ 2 km
R
x=?

## Slide 60: CONCEPTS: CELLULAR
27
Reuse factor Q:
Q  D
R
D: distance between cells using the same
frequency
R: cell radius
For hexagonal cells,
D
R
Q  D  3N
R
cluster size
– E.g. N = 7, Q =
21  4.58
Q   spatial separation relative to cell coverage   CCI   Good
Q   N   bigger cluster size  less frequency reuse (or, less clusters)
 smaller capacity  less users can be served  Bad
Tradeoff between: voice quality and system capacity

## Slide 61: CONCEPTS: CELLULAR
29
Advantages of Cell with Frequency Reuse
  Limited frequency resource can be reused to support unlimited number of
users
    Each cell support only limited number of users
    The number of users supported by system increase linearly with the number of cells
  Each BS only covers one cell
    Smaller Tx power at BS  Less interference to other systems
    Smaller Tx power at MS  Longer battery life
  A cell can be further divided into smaller cells to support more users
    Upgradability
Disadvantage:
  Cells sharing same frequency will interfere with each other  co-channel interference (CCI)
  We want cells sharing same frequencies to be as further away as possible.

## Slide 62: OUTLINE
30
Background
Major modern wireless communication standards
Basic Concepts
Block diagrams of a wireless communication system

## Slide 63
Department of Electrical Engineering
University of Arkansas
ELEG 5693 Wireless Communications
Propagation and Noise Part I
Dr. Jingxian Wu
wuj@uark.edu

## Slide 64: OUTLINE
2
Wireless channel
Path loss
Shadowing
Small scale fading
Channel classifications
Noise and interference
Simulation model

## Slide 65: BLOCK DIAGRAM of WIRELESS COMMUNIICATION SYSTEM
31
Source Coding
Channel Coding
Modulation
Channel
Demodulation
Equalization
Channel Decoding
Source Decoding
Transmitter
Receiver

## Slide 66: CHAPTER 2: Path Loss, Shadowing, and Multipath
3

## Slide 67: CHANNEL: PROPAGATION MODES
4
Free-space (line-of-sight)
  There is a clear transmission path between transmitter (Tx) and
receiver (Rx).
  E.g. satellite
Reflection
  The bouncing of electromagnetic waves from surrounding objects
  Size of reflecting objects must be large compared to the wavelength of signal
  Reflecting surface must be smooth compared to the wavelength of
signal
  E.g. ground, building, walls, windows, lakes

## Slide 68: CHANNEL: PROPAGATION MODES
5
Diffraction
  The bending of electromagnetic waves around objects (such as buildings), or through objects (such as trees).
  Due to diffraction, signals can propagate
    Around curved surface of Earth
    Beyond LOS horizon
    Behind obstructions
Scattering
  Electromagnetic waveforms incident upon rough or complex surfaces are scattered in many directions
    Relfection: smooth surface, one direction
Refraction (not common in terrestrial wireless communication).
  Electromagnetic waves bend as they move from one medium to another.

## Slide 69: CHANNEL
6
Wireless channel: propagation, noise and interference
  Propagation effects: line-of-sight, reflection, diffraction, scattering
    Induced by the transmission of desired signals itself
    Impairments: large scale fading (path loss, shadowing), small
scale fading
    Unique to wireless communication
  Noise and interference: unwanted electrical signals interfering with
desired signal.
Thermal noise (movements of electrons)
Automobile ignition, electrical machinery, etc.
Interferences from other users operating on the same frequency.
Channel: a collection of propagation effects and other signal impairments caused by the environments
Present in all communication systems

## Slide 70: OUTLINE
7
Wireless channel
Path loss Models
Shadowing
Multipath Fading
Small scale fading
Channel classifications
Noise and interference
Simulation model

## Slide 71: PATH LOSS
8
Path loss: the power loss during signal propagation from Tx to Rx
– Only a portion of the power from Tx will be captured by the receiver.
p
P
L
 PT
R
Path loss is defined as the ratio between the signal power at
transmitter (PT) and signal power at receiver (PR).
R
p
10 R
10 T
PT
10 P
P 10 log P
 10 log
L (dB)  10 log

## Slide 72: PATHLOSS: MODELS
9
Free-space path loss model
  Clear, unobstructed LOS.
  Doesn’t consider surrounding objects.
  Highly simplified model
  Received signal is
        Receiver power is
Notes: Gt and Gr are, respectively, the transmit and receive antenna power gains in the LOS direction relative to a unity gain isotropic antenna, τl = d/c is the signal propagation delay of the LOS signal traveling the distance d, and the phase shift e −j2πd/λ is due to the distance d that the wave travels2

## Slide 73: PATHLOSS: MODELS
9
Two Ray-tracing models
  Consider the effects of reflection, diffraction from surrounding environment
  More complex, depends on site geometry
  At small distances, power falls off proportional to d2 (free space loss on both paths). for asymptotically large d, d1 ≈ d0 ≈ d, G1 ≈ G0, received power given by Pr
  Above dc, power falls off proportional to d 4 and is independent of signal wavelength (frequency)

## Slide 74: PATH LOSS: EXPONENT MODEL
16
A general model capturing the essence of path loss in various environment
dr
: reference distance (typically 1 meter)
0 : a unitless constant equal to the path gain Pr/Pt at distance d = dr
γ : path loss exponent (can be obtained through measurement)
d : distance between transmitter and receiver
Multi Slope
– The multi-slope path loss model, which is piecewise linear in dB, generalizes the single-slope model by allowing for different path loss exponents at different distances

## Slide 75: OUTLINE
19
Wireless channel
Path loss
Shadowing
Small scale fading
Channel classifications
Noise and interference
Simulation model

## Slide 76: SHADOWING
20
Shadowing:
  Caused by large obstructions that are distant from MS
  Effects of shadowing is random due to random # and type of obstructions.
  The existence of shadowing is verified through field measurement.
  Typically follows a log-normal distribution

## Slide 77
21
COMBINED PATH LOSS AND SHADOWING
dB representation
S(dB)  10log10 S : follows Gaussian distribution (normal distribution)
•



)2 
 2 
dB
dB
1 (x  m
fS (dB) (x)  exp  dB 
2
2
S(dB) follows normal distribution the log of S follows normal distribution
 The distribution of S is called lognormal distribution
Shadowing is called lognormal shadowing

## Slide 78: COMBINED PATH LOSS AND SHADOWING
22
combined effects of path loss and shadowing (red curve)
path loss only
path loss with shadowing (random)

## Slide 79: OUTAGE PROBABILITY
22
With path loss and shadowing, the received power at any given distance between transmitter and receiver is random.
Leads to a non-circular coverage area around the transmitter, i.e. non-circular contours of constant power above which performance (e.g. in WiFi or cellular) is acceptable
Outage probability: probability received power falls below given minimum:
For log-normal shadowing model

## Slide 80: CHAPTER 3: Statistical Multipath Channel Models
3
Notes: Chapter 2 for deterministic channels, we rarely have sufficiently precise knowledge about wireless propagation environments to characterize them deterministicallyThis chapter develops a statistical characterization of Wireless channel model and describes its important properties.

## Slide 81: FADING: WHAT IS FADING?
4
Random # of multipath components
– The amplitude, phase, and frequency of each component change
w.r.t. the movement of MS.
The signal at the receiver is the summation of all the multipath components  the amplitude, phase, and frequency of the received signal at receiver change w.r.t. the movement of MS.
The movement of surrounding objects (e.g. vehicles) will also cause the time variation of the signals.

## Slide 82: DOPPLER
6
What is Doppler?
  The whistle of the train coming from opposite direction sounds different with the train passing by.
    The pitch of the sound (determined by sound frequency) is changing.
  Rx signal frequency will change if the Rx is moving w.r.t. Tx.
  Signal frequency change due to the relative movement between Tx and Rx is called Doppler effects.
t=0
t=0.5s
t=1s
T = 1s
T = 0.5s
a
b
c
c
b
a
a
b
c
a
c b
c
b
a
a
b
c

## Slide 83: DOPPLER
7
Consider Tx sends out a sinusoid with frequency 1Hz
  If Rx moves toward Tx, the signal observed by Rx will have a
shorter period  frequency increased
  If Rx moves away from Tx, the signal observed by Rx will have a longer period  frequency decreased
The amount of frequency change is called Doppler shift
  Doppler shift depends on
    Relative speed between Tx and Rx
    The frequency of the original signal

## Slide 84: Statistical Multipath Model
• At each time instant there are a random number N(t) of multipath signal components.
• At time t the ith component has a random amplitude αi(t), angle of arrival θi(t), Doppler shift fDi = (v /λ) cos θi(t) and associated phase shift φDi and path delay relative to the LOS component τi(t) = (xi(t))/c.
• Thus, the received signal is given by the following expression, which implies the channel has a time-varying impulse response

## Slide 85
10
FADING: IMPULSE RESPONSE
The impulse response of fading is time-varying!
N
c(t, )  n (t) cos2fct  n (t) (  n )
n1
fc : system operating frequency (e.g. 900MHz, 1.8GHz)
t: the time variation (both amplitude and phase changes with respect to time)
 : relative delay between multipath components
n (t) : depends on path distance and Doppler shift 2fDt 
Relative multipath delay 
Time variation t
N multipath components

## Slide 86: Received Signal Characteristics
• The received signal consists of N multipath components scaled by amplitude αn(t) and phase φn(t) = 2πfcτn(t) − φDn (t).
• The amplitude term αn(t) varies slowly (due to shadowing).
• The phase φn(t) varies rapidly due to small shifts in the signal component path delays.
• The phase variation causes rapid variation in the received signal amplitude due to constructive and destructive interference of the multipath components.

## Slide 87: FADING: WHAT IS FADING?
3
Path loss and shadowing is caused by large objects that are distant from MS.
  Even the MS is moving, the change in the relative position between MS
and those distant large objects is small.
  Therefore, the impairments caused by those large distant objects change very slow with respect to (w.r.t.) time and position.
  Shadowing is also referred to as large scale fading.
Small scale fading is caused by the effects of objects that are close
to MS.
  The movement of MS w.r.t. nearby small objects will dramatically change the reflection or diffractions of propagated signals.
  The signal at receiver (sum of the signals from all multiple paths) will change rapidly with the movement of MS.
Small scale fading: rapid fluctuation of the received signals over short distance.

## Slide 88
12
FADING: FLAT FADING (Narrowband Model)
Flat fading
Maximum delay spread  max << system symbol period Ts
Relative to the symbol period, all the multipath components arrive at almost the
same time  Doesn’t need to consider the delay variable 
N
n
n
 n
N N
 n
n
 n n1
n1
(t)e
 (t)
 (t) j   (t) sin
  (t) cos
n1
h(t)  
j (t )
N
n
I
 n n1
 (t)
h (t)   (t) cos
– Inphase component
– Quadrature component
N
n
Q
 n n1
 (t)
h (t)   (t) sin
Maximum delay spread
– The time interval between the first multipath and the last multipath
 max
 N 1

## Slide 89: FADING: FLAT FADING
13
h(t)  hI (t)  j  hQ (t)
Both hI(t) and hQ(t) are the sum of many multipath components
  Each multipath component is a random process
  hI(t) and hQ(t) are random processes
Central limit theorem
  The sum of N independent and identically distributed (i.i.d.) random variables tends to Gaussian distribution when N is large enough.
Based on central limit theorem, at time time t, both hI(t) and hQ(t) are
Gaussian distributed!

## Slide 90
14
FLAT FADING: RAYLEIGH FADING
If there is no LOS between Tx and Rx
hI(t) and hQ(t) are zero-mean Gaussian distributed
The amplitude (or envelope) of h(t)
~ N (0, 2 )
h(t)  h2 (t)  h2 (t)
I Q
– The fading envelope |h(t)| follows Rayleigh distribution


 
2
2
exp 

2

z2
z
f (z) 
h(t )
– Average power of fading
2
2
2
2
2
Eh (t) 
Eh (t)
Eh(t) 
Q
I

## Slide 91: FLAT FADING: RICIAN FADING
15
If there is LOS component
hI(t) and hQ(t) are non-zero-mean Gaussian distributed
The fading envelope
~ N (s, 2 )
h(t)  h2 (t)  h2 (t)
I Q
follows Rician distribution

## Slide 92
16
FLAT FADING: TIME DOMAIN CORRELATION
The time domain correlation of h(t) is
*
D
h h 0
f  )
R ()  Eh(t  )h (t) P  J (2
– J0(x): zero-order Bessel function of the first kind
Fd = 10Hz
Fd = 50Hz
Generally speaking, for given time interval 
  Larger speed v  larger fD  smaller| Rh ( ) | .

## Slide 93: SIMULATOR
20
How to generate flat Rayleigh fading with computer program?
  Method 1: Filtered Gaussian noise
    Rely on low-pass filter to introduce the time-domain correlation among symbols
White
Gaussian
Low-pass
Filter
White
Gaussian
Low-pass
Filter
hI(t)
hQ(t)
– The low-pass filter is hard to design.

## Slide 94
Received signal can be written in terms of in-phase and quadrature components as
where and
where now also incorporates phase of the
Transmitted signal.
If large then in-phase and quadrature signal components are jointly Gaussian
(amplitude of scale factor is Rayleigh).
Thus, received signal characterized by mean, autocorrelation, and cross correlation.
Assuming uniform, and .
In-Phase and Quad Signal Components under CLT

## Slide 95
Mean, Autocorrelation, and Cross Correlation in Flat Fading
Assuming uniform, and . Thus,
and are uncorrelated, hence independent. Moreover,
, so the
processes are WSS and hence stationary. Note that . , the total average
received power.
Using a similar analysis, get
.
Using these derivations, we get the autocorrelation for the received signal as
.
Since this only depends on , the received signal is WSS and hence stationary.

## Slide 96
Under uniform scattering the s are uniformly distributed. We also assume all multipath components have the same expected power, so for the total received power and the number of multipath components. With these assumptions the in-phase and quadrature signal components have zero cross correlation and have autocorrelation .
Thus the signal decorrelates over roughly one half of a wavelength, but later recorrelates.
Can obtain the PSD of the received signal by taking the Fourier transform of its autocorrelation. Power spectral density
This yields where
The PSD is useful in simulating fading channels.
Correlation and PSD under Uniform Scattering

## Slide 97
CLT approximation leads to Rayleigh distribution (in-phase and quadrature zero mean and jointly Gaussian): .
Obtain power distribution by making the change of variables to obtain .
A LOS component leads to a received signal with non-zero mean. The Rician distribution models signal envelope in this case, with factor dictating the relative power of the LOS component: .
Experimental results support a Nakagami distribution for some environments. Similar to Rician, but can model "worse than Rayleigh." Model generally leads to closed-form expressions in BER and diversity analysis.
Distribution is . By change of variables, power distribution is .
. Signal Envelope Distributions

## Slide 98
In wideband multipath channels the individual multipath components can be resolved by the receiver. True if .
If the components can be resolved then they can be combined for diversity gain (e.g. using an equalizer).
Typically time-varying channel impulse response is unknown, so its wideband model must be characterized statistically.
Since under our random model with a large number of scatterers, is Gaussian, only need to characterize its mean and correlation, which we show is independent of time (wide-sense stationary or WSS). Similar to narrowband model, for uniformly distributed, has mean zero.
wideband

## Slide 99: CLASSIFICATION
23
Fading
  Amplitude and phase distortions of transmitted signal
Classification criterions
  Scale
    Large scale fading, small scale fading
  Small scale fading
    Flat fading v.s. frequency selective fading
    Fast fading v.s. slow fading
    Rayleigh fading v.s. Rician fading

## Slide 100: CLASSIFICATION: FAST FADING V.S. SLOW FADING
25
The time domain variation of fading is determined by maximum Doppler spread fD
  Doppler shift: signal frequency change due to relative movement between Tx and Rx.
  Larger speed v  larger fD  channel varies faster.
Coherence time Tc
  The time period over which the channel is strongly correlated (didn’t change
too much)
– Inverse proportional to fD
D
c
1
2 f
T 
Tc
Tc

## Slide 101
29
CLASSIFICATION: FLAT V.S. FREQUENCY SELECTIVE
Coherence bandwidth Bc
  The bandwidth over which the channel is strongly correlated (didn’t change too much)
    The spectrum over coherence bandwidth is almost “flat”
  Inverse proportional to rms delay spread
rms
c
2
1
B 
Bc
(Coherence bandwidth Bc, rms delay spread  rms ) is related to fast fading or slow fading
f

## Slide 102: CLASSIFICATION: FAST FADING V.S. SLOW FADING
26
System symbol period v.s. signal bandwidth
0
0 1 0 0 1 0 1
Symbol Period = Ts
Signal BW = Bs  1 / Ts
Fast fading
  If Ts > Tc, or Bs < fD
    Ts > Tc: channel changes within one symbol period fast fluctuation
Slow fading
  If Ts << Tc, or Bs >> fD
    Ts << Tc : channel keeps constant during several symbol periods 
slow amplitude fluctutation.
(Coherence time Tc, Doppler spread fD) is related to fast fading or slow fading

## Slide 103
28
CLASSIFICATION: FLAT V.S. FREQUENCY SELECTIVE
Maximum delay spread
– The time interval between the first multipath and the last multipath
Mean delay spread
 max
 N 1
Root mean square (rms) delay spread
N
n
total
n
P
P

n1

 
n
P : the average power of the nth multipath

N
N
n
rms 
n
P
Pn
total
P
Pn
total
n1
n1
2
 2  2
    
 
N
n1
total  n
P :
P 
the total power of the all multipath

## Slide 104
fc
30
CLASSIFICATION: FLAT V.S. FREQUENCY SELECTIVE
Flat fading – Narrowband Model
  If Bs << Bc, or Ts >>  rms
  Bs << Bc: signal bandwidth << channel bandwidth
  Ts >>  rms : relative arrival time between multipath components is negligible
    Doesn’t need to consider delay variable h(t, )  h(t)
Bc
Bs
f
Frequency selective fading - Wideband model
If Bs >> Bc, or Ts <<  rms
Bs >> Bc: signal bandwidth >> channel bandwidth
  Signal spectrum will be seriously distorted by channel!
Ts <<  rms : symbol period smaller than rms delay spread
  The relative arrival time between the multipath components is no longer negligible!

## Slide 105: CLASSIFICATION: FREQUENCY SELECTIVE FADING
31
Frequency selective fading
– rms delay spread
> system symbol period Ts
 rms
The relative arrival time between the multipath components is no longer negligible!
The N multipath components are divided into L clusters
  Within each cluster, there are still many multipath components
  Multipath components belonging to the lth cluster arrives at approximately the same time  l .
L L
l l Il Ql l
(t) (  )
h(t, )  h (t)  (  )  h (t)  jh
l 1 l 1
hl(t) is the sum of all the multipath components within the same cluster
  Resolvable multipath component
The inphase and quadrature components of hl(t) are Gaussian distributed.
The frequency selective fading can be viewed as the combination of multiple flat fading
  Each branch (cluster) hl(t) can be viewed as flat fading

## Slide 106
32
CLASSIFICATION: FREQUENCY SELECTIVE FADING
Each branch of frequency selective fading can be viewed as a flat fading
  All the properties discussed for flat fading can be directly applied
to each branch of frequency selective fading
    E.g. Inphase and quadrature components are Gaussian distributed.
    fading envelope: Rayleigh v.s. Rician

## Slide 107
33
CLASSIFICATION: FREQUENCY SELECTIVE FADING
Relative multipath delay 
Time variation t

## Slide 108: CLASSIFICATION: RAYLEIGH V.S. RICIAN
36
Fading envelope
h(t)  h2 (t)  h2 (t)
I Q
Rayleigh fading
  Fading envelope |h(t)| follows Rayleigh distribution
  Non LOS (no dominant multipath components)
Rician fading
  Fading envelope |h(t)| follows Rician distribution
  One dominant component (LOS) along with weaker multipath signals

## Slide 109
Multipath Intensity Profile and Delay Spread
Multipath intensity profile (delay power spectrum) defined as , i.e. the autocorrelation relative to delay at a fixed time.
The average delay and rms delay spread are defined relative to . These parameters approximate the maximum delay of nontrivial multipath components.
Coherence Bandwidth
The coherence bandwidth is defined relative to the Fourier transform of , given by . Note that .
Since is the autocorrelation of a Gaussian process, multipath components separated by are independent if .
By the Fourier transform relationship, the bandwidth over which is nonzero is roughly or (can also add constants to these denominators).
defines the coherance bandwidth of the channel, i.e. the bandwidth over which fading is correlated.
A signal experiences frequency selective fading or ISI if its bandwidth exceeds the coherence bandwidth of the channel.
Doppler Power Spectrum, Doppler Spread, and Coherence Time:
Doppler power spectrum is defined with respect to .
Specifically, the Doppler power spectrum is , which measures channel intensity as a function of Doppler frequency.
The maximum value of for which is called the channel Doppler spread, which is denoted by .
By the Fourier transform relationship, for . Thus, the channel becomes uncorrelated over a time of seconds.
We define the channel coherance time as . A deep fade lasts approximately seconds. Hence, if the coherence time greatly exceeds a bit time, the signal experiences error bursts lasting seconds.
Notes: Fama hajet zidhom note 6

## Slide 111: NOISE
38
Noise and interference
  Unwanted electrical signals interfering with the desired signal
  Arises from outside natural or artificial sources
    Artificial source: noise from automobile ignition, signal from other communication system, etc.
    Natural source: thermal noise, atmospheric disturbances.
Noise v.s. fading
  Noise arises from outside sources
    fading arises from the signal propagation itself
  Noise is added to the desired signal  the desired signal is buried by noise
(noise only has negative effects on signal).
    Fading results in signal power fluctuation  signal power may become larger or become smaller (fading might benefit system performance).
  Noise is present in all communication systems.
    Fading is unique to wireless communications.

## Slide 112: NOISE: SIGNAL TO NOISE RATIO
39
Signal to noise ratio (SNR):
  the ratio of the signal power to the noise power at the receiver.
  SNR = S/N, with S being the signal power, and N being the noise
power observed by the receiver.
  High SNR  Signal is strong, and noise is weak  Better communication quality.
  Improve SNR  Improve Tx power  More power consumption
High SNR
Low SNR

## Slide 113: NOISE: THERMAL NOISE
41
Thermal noise is a random process
  At any time instant, the random voltage due to thermal noise follows Gaussian distribution with zero mean.
    The random voltage is caused by the sum of the motions of a large number of electrons (central limit theorem).
  The noise samples at any two different time instants are uncorrelated. Auto- correlation function
2
0
*
 ( )
N
x
R ( )  En(t)n (t  )

## Slide 114
42
NOISE: THERMAL NOISE
Power spectral density
– Fourier transform of autocorrelation function
2
2
0
N
x
 N

S ( f ) 
0  ( )e j 2f d 
f
SX  f 
N0/2
RX ( )
N0/2

white spectrum
Additive White Gaussian Noise (AWGN)

## Slide 115: NOISE: COCHANNEL INTERFERENCE
43
Cochannel interference (CCI)
  Due to frequency reuse, cells using the same frequency range will
generate interference with each other.
  Unique to cellular system.

## Slide 116
3
CHAPTER 4: Capacity of Wireless Channels

## Slide 117
Shannon Capacity
The maximum mutual information of a channel. Its significance comes from Shannon's coding theorem and converse, which show that capacity is the maximum error-free data rate a channel can support.
Capacity is a channel characteristic - not dependent on transmission or reception techniques or limitation.
In AWGN, , where is the signal bandwdith and is the received signal-to-noise power ratio.
Capacity of Flat-Fading Channels:
Depends on what is known about the channel.
Three cases: 1) Fading statistics known; 2) Fade value known at receiver; 3) Fade value known at transmitter and receiver. 1 - When only fading statistics known, capacity difficult to compute. Only known results are for Finite State Markov channels, Rayleigh fading channels, and block fading. 2 4. Fading Known at the Receiver:
Capacity given by bps, where is the distribution of the fading SNR .
By Jensen's inequality this capacity always less than that of an AWGN channel.
"Average" capacity formula, but transmission rate is fixed. 5. Capacity with Fading Known at Transmitter and Receiver
For fixed transmit power, same capacity as when only receiver knows fading.
Transmit power as well as rate can be adapted.
Under variable rate and power , where is power adaptation
Optimal Power and Rate Adaptation
Optimal adaptation found via Lagrangian differentiation.
Optimal power adaptation is a "water-filling" in time: power increases with channel quality above an optimized cutoff value .
Rate adaptation relative to is : also increases with above cutoff.
Resulting capacity is .
Capacity with power and rate adaptation not much larger than when just receiver knows channel, but has lower complexity and yields more insight into practical schemes.
Capacity in flat-fading can exceed the capacity in AWGN, typically at low SNRs.

## Slide 122
3
CHAPTER 5: Digital Modulation and Detection

## Slide 123: OUTLINE
2
Modulation
Linear Modulation I
Complex Signal Representation
Pulse Shaping
Linear Modulation II
Non-linear Modulation
FDMA

## Slide 124
3
MODULATION: DEFINITION
What is modulation?
  The process of modifying a carrier signal (usually a sinusoid) in accordance with an information-bearing signal (modulating signal), such that the modified carrier signal (modulated signal) can be used to convey information.
  Carrier signal:
c(t)  Ac sin(2fct  )
Three parameters: amplitude, frequency, phase
One or all of them can be modified to carry information.
– E.g. the amplitude is modified to carry information m(t)
s(t)  m(t)Ac sin(2fct  )
Modulator
m(t)
s(t)

## Slide 125: MODULATION: DEFINITION
4
What is modulation? (cont’d)
  Modulating signal m(t)
    Original electrical information-bearing signal
    E.g. electrical waveform representing voice, ASCII, digital video, etc.
    Usually at low frequency
    Also called baseband signal
  Carrier signal c(t)
    High frequency sinusoid to carry the information.
  Modulated signal s(t)
    Carrier signal modified by modulating signal
    At the output of the modulator.
    Also called bandpass signal, or RF signal
Modulator
c(t)
m(t)
s(t)

## Slide 126: MODULATION: WHY?
5
Why modulation?
  Shift the frequency of the message signal to the pre-allocated channel.
    For example:
      speech signal: 300 ~ 3100 Hz m(t)
      Shift the signal to the allocated frequency range: 900MHz c(t)
  Transfer the message into a form more suitable for wireless
transmission.
    Limited bandwidth
    Make better use of the limited spectrum
    High frequency signals are more suitable for wireless transmission.
  Enables multiple access
    Signals from different users can be shifted to different frequencies.
    Modulation allows the simultaneous transmission of multiple users.

## Slide 127: MODULATION: TERMS
6
Demodulation
  Recover the original message signal m(t) from the modulated signal s(t).
Modulator
  Device used to perform modulation
Demodulator
  Device used to perform demodulation.
s(t) r(t)
Modulator
Demodulator
m(t)
mˆ (t)
r(t): modulated signal impaired by fading and noise.

## Slide 128: MODULATION: CLASSIFICATIONS
7
Linear modulation v.s. non-linear modulation
Analog modulation v.s. Digital modulation
Amplitude modulation v.s. Angle modulation

## Slide 129
8
MODULATION: LINEAR V.S. NON-LINEAR
Principle of superposition
Modulator
mi(t)
si(t)
If the input-output of the modulator satisfies principle of superposition, then the modulator is called linear modulator.
– E.g.
s1 (t)  s2 (t)
If input is m1 (t)  m2 (t) , then output is
If input is a  m1 (t) , then output is a  s1 (t)
s(t)  m(t)Ac sin(2fct  )
If the principle of superposition is not satisfied, the modulator is
non-linear modulator.

## Slide 130: MODULATION: ANALOG V.S. DIGITAL
9
Analog modulation
  m(t) is an analog signal
    m(t) is a continuous function of time t.
    m(t) can take infinite number of values
  Analog modulation is also called continuous-wave (CW) modulation.
  AM radio, FM radio, first generation cell phone system
Digital modulation
  m(t) is a digital signal
    Take finite number of values
    E.g. {-1, 1}, {-2, -1, 1, 2}, …
  2nd generation cell phone system
  Digital modulation systems have become more and more popular.

## Slide 131: MODULATION: AMPLITUDE V.S. ANGLE
10
Amplitude modulation
  The amplitude of the carrier, Ac , is modified by the message
signal m(t).
Angle modulation
  The angle of the carrier is modified by the message signal m(t).
 (t)  2fct 
  Frequency modulation: frequency is modified by m(t).
  Phase modulation: phase is modified by m(t)

## Slide 132: OUTLINE
11
Modulation
Linear Modulation Techniques I
Complex Signal Representation
Pulse Shaping
Linear Modulation Techniques II
Non-linear modulation
FDMA

## Slide 133: LINEAR MODULATION: AM
12
Amplitude modulation (AM)
– The term, AM, is usually used when m(t) is analog
s(t)  Acm(t) cos(2fct)
message signal
carrier frequency
Spectrum of AM
–

–
Ac cos(2fct) 
– s(t)  S(f) = ?
m(t) M ( f )
2
c
c
 ( f  f )   ( f  f )
c
A

## Slide 134: LINEAR MODULATION: AM
13
-W
W
f
0
M(f)
S(f)
f
fc W
fc fc W
 fc
 fc W
 fc W
Center frequency shifted from 0 to
The bandwidth is doubled from W to 2W
fc
Spectrum of AM
Baseband signal
bandpass signal

## Slide 135: LINEAR MODULATION: AM
14
Bandwidth
  Baseband bandwidth (bandwidth of baseband signal): from 0 to W
  Passband bandwidth (bandwidth of modulated signal): from Fc-W to Fc+W.
    Passband bandwidth is twice of baseband bandwidth.
How do we define bandwidth?
  There are many different definitions of bandwidth
  B’: half power bandwidth (3dB bandwidth).
  B’’: null-to-null bandwidth
  B’’’: absolute bandwidth
  FCC definition: bandwidth contains 99% of signal power
f
B’
fc
B” B”’
1
0.5
power spectrum

## Slide 136: LINEAR MODULATION: BPSK
15
Binary phase shift keying (BPSK)  Digital modulation
for binary 1
for binary 0
A cos(2f t   )
s(t)  
 c c
Ac cos(2fct)
– Or alternatively
for binary 1
for binary 0
 c c
 A cos(2f t)
s(t)   Ac cos(2fct)
– Also called binary amplitude shift keying (BASK)

## Slide 137: LINEAR MODULATION: BPSK
16
1
1
1
0
1
m(t)
-1
s(t)
s(t)  m(t) sin(2fct)

## Slide 138
17
LINEAR MODULATION: BPSK

m(t)  bk p(t  kTs )
k 1

1
k
b   1

0  t  T
0 o.w.
p(t)  1
0 Ts
p(t)
(k+1)Ts
kTs
p(t-kTs)
Ts: symbol period. (The time duration to carry one symbol)
usually inverse proportional to signal BW

## Slide 139: LINEAR MODULATION: MASK
18

m(t)  mk p(t  kTs )
k 1
mk {s1, s2 ,, sM }

0  t  T
0 o.w.
p(t)  1
M-ary amplitude shift keying (MASK)
– The information can take
values
E.g. 4-ary amplitude shift keying (4ASK)
mk  {3,1,1,3}
M  2n

## Slide 140: LINEAR MODULATION: MASK
19
-1
1
-1
-3
m(t)
1
-3
3
s(t)
(11)
(10)
3
(00)
(01)

## Slide 141: LINEAR MODULATION: MASK
20
Each symbol can take M values
Each symbol can represent n  log2 M bits of information.
E.g.
  4ASK  M = 4  2 bits/sym
  8ASK  M = 8  3 bits/sym
  16ASK  M = 16  4 bits/sym
Symbol rate (baud) Rs :
  # of modulation symbols/second
  Generally, signal bandwidth is proportional to symbol rate!
Bit rate Rb:
  Bits/second
Rb = Rs x (# of bits/sym)

## Slide 142: LINEAR MODULATION: MASK
21
M-ary modulation
  At the same symbol rate, (or fixed bandwidth)
    Larger M  more bits/symbol  larger bit rate
  M-ary modulation is good for band-limited system
    In wireless systems, spectrum is precious
    M-ary modulation is widely used in wireless systems!
    Typical values used in wireless system: M = 2, 4, 8, 16
Why don’t we use a very large M?
  If M  infinity, then analog signal
  At the same SNR
    Larger M  signals are more closed to each other  it’s harder to distinguish between all signals at receiver due to noise  probability of error becomes larger!

## Slide 143
22
LINEAR MODULATION: QPSK
Quadrature phase shift keying (QPSK)
  Combination of two BPSK streams
  Quadrature: orthogonal (two carriers that are 90 degree apart)
m1 (t)
Ac cos(2fct)
m2 (t)
Ac sin(2fct)
s(t)  Acm1 (t) cos(2fct)  Acm2 (t)sin(2fct)
s(t)
Inphase signal
quadrature signal

## Slide 144
23
LINEAR MODULATION: QPSK
Demodulator
– How could these two signals not interfere with each other?
2
A m (t)sin(2
A m (t) cos (2
c
c
c 2
c
c 1
c
f t)
f t) cos(2
s(t) cos(2
f t) 
f t) 
2
2
2
2
1
1
m (t) sin(4
A
m (t) cos(4
A
A
c
c
c
c
c
f t)
f t) 
m (t) 

2
1
m (t)
A
c
m1 (t)
m2 (t)
Ac cos(2fct)
Ac sin(2fct)
low pass filter
low pass filter
s(t)
After low pass filter:

## Slide 145: LINEAR MODULATION: QPSK
24
At each symbol period, two bits of information are transmitted
2 bits/symbol
Inphase signal sI (t)  Acm1 (t) cos(2fct) has the same bandwidth as BPSK
Quadrature signal sQ (t)  Acm1 (t) sin(2fct) has the same bandwidth as BPSK
The sum has the same bandwidth as BPSK
Sum in time domain  sum in frequency domain  bandwidth unchanged.
The same bandwidth as BPSK, but twice the bit rate of BPSK!
No interference between quadrature and inphase
  Inphase has the same error performance as BPSK
  Quadrature has the same error performance as BPSK
  QPSK has the same error performance of BPSK!
s(t)  sI (t)  sQ (t)
One of the rare occasions that increase bit rate without sacrificing error performance!

## Slide 146: OUTLINE
25
Modulation
Linear Modulation Techniques I
Complex Signal Representation
Pulse Shaping
Linear Modulation Techniques II
Non-linear modulation
FDMA

## Slide 147
26
COMPLEX REPRESENTATION
Band-pass signal
s(t)  sI (t) cos(2fct)  sQ (t)sin(2fct)
Complex base-band signal (also called the complex envelope of the
signal)
~s (t)  s (t)  js (t)
I Q
Relationship between complex baseband and band-pass
s(t)  Re~s (t) exp( j2fct)

## Slide 148: COMPLEX REPRESENTATION
27
Modulation can be decomposed into two steps:
  1. complex baseband modulation, 2. frequency upconversion
    The complex representation completely preserves the information of the modulating signal except the carrier frequency
  It’s suffice for us to examine baseband modulation only!
s(t)  Re~s (t) exp( j2fct)
Frequency
upconversion
Baseband
modulation
Modulation

## Slide 149
28
COMPLEX REPRESENTATION: BASEBAND MODULATION
BPSK
sI (t) {1,1}
s (t) {1,1}
I
sQ (t)  0
QPSK
sQ (t) {1,1}
~s (t) {1,1}
~s (t) {1 j,1 j,1 j,1 j}
(M  2)
(M  4)
Frequency
upconversion
Baseband
modulation
Modulation

## Slide 150
29
COMPLEX REPRESENTATION: CONSTELLATION
Modulation Constellation
  The collection of all modulation symbols in their complex representation.
  Es : the energy of one symbol
QPSK
~
Es exp( j )
 Es exp( j0),
s (t) 









4 
, 
 4  
7 
4
5
4
3  

~s (t)  
), Es exp  j
Es exp( j
Es exp  j
Es exp( j ),
Re
Im
BPSK
 Es
Es
0
1
Re
Im
Es
00
01
10
11

## Slide 151: COMPLEX REPRESENTATION
30
Re
Baseband modulation examples
Im
 Es
Es
0
1
Re
Im
s
E
00
01
10
11
BPSK
0010110111
BPSK:
QPSK:

## Slide 152
31
COMPLEX REPRESENTATION: SYMBOL ENERGY
Symbol energy Es
– If modulation symbol is
~s (t) 
Es exp j (t)
The energy of one symbol is Es
  Proof:
.
Bit energy Eb
The energy of one bit
# of bits per symbol:
Eb  Es / log2 M
log2 M

## Slide 153: COMPLEX REPRESENTATION
32
Signals pass through channel with flat fading and AWGN
h
~
I Q
h (t)  h (t)  jh (t)
: time-varying flat fading
n~(t)  n (t)  jn (t)
I Q
: AWGN
Both the inphase component and quadrature component are going to be distorted.

## Slide 154: COMPLEX REPRESENTATION: SNR
33
Signal to noise ratio (SNR)
  The ratio between signal power and noise power
  E.g. same level of noise, signal power becomes smaller
SNR=15dB
SNR=10dB
SNR=5dB
SNR=0dB
~y(t)  ~s (t)  n~(t)
QPSK:

## Slide 155: COMPLEX REPRESENTATION: SNR
34
Baseband demodulation
  Find the modulation symbol that has the smallest Euclidean distance with the
received signal.
  E.g. QPSK: r = x + n
r = 0.3 + j 0.5
Re
Im
| 0.3  j0.5  exp( j / 4) |2  0.2086
| 0.3  j0.5  exp( j3 / 4) |2  1.0572
| 0.3  j0.5  exp( j5 / 4) |2  2.4714
| 0.3  j0.5  exp( j7 / 4) |2  1.6228

## Slide 156: COMPLEX REPRESENTATION: SNR
35
SNR
– The ratio between signal power and noise power
Pn N0 B
Ps Es / Ts
SNR 

Power spectral density of noise
Signal bandwidth
Symbol period
 Rs  Eb  Rs log2 M  Eb  Rb
SNR  Es
N0 B N0 B N0 B
Symbol rate Rs = 1/Ts
Bit rate Rb

## Slide 157: COMPLEX: BANDWIDTH EFFICIENCY
36
Bandwidth efficiency
– How many bits can be accommodated in unit bandwidth (bps/Hz)
B
R
B  b
bit rate
bandwidth
Measures the ability of the modulation technique to accommodate data in a limited bandwidth
  Larger bandwidth efficiency  more data can be transferred in limited bandwidth
Generally, the bandwidth is proportional to symbol rate
B  Rs
  For M-ary modulation, fixed bandwidth B  fixed symbol rate Rs
    Larger M  larger Rb  Rs log2 M  larger bandwidth efficiency

## Slide 158: COMPLEX: ENERGY EFFICIENCY
37
Energy efficiency
  At given noise level, how much energy is required to achieve a
certain bit error rate.
  Measured as the value of Eb/N0 required for certain bit error rate (BER).
    Eb: energy per bit. N0: noise power spectral density.
Eb/N0 (dB)
BER
BER v.s. Eb/N0 is the most important
measure of digital communication systems!

## Slide 159: OUTLINE
38
Modulation
Linear Modulation Techniques I
Complex Signal Representation
Pulse Shaping
Linear Modulation Techniques II
Non-linear modulation
FDMA

## Slide 160: PULSE SHAPING
39
Why pulse shaping?

k 1
 k s
m(t)  m p(t  kT )

0 o.w.
– In previous discussions, the message m(t) is represented as a series
rectangular pulses.
0  t  T
p(t)  1
1 0
1
1
1
m(t)
-1
– Rectangular pulse has unlimited bandwidth!
t
f
Fourier Transform

## Slide 161: PULSE SHAPING
40
Why pulse shaping? (Cont’d)
  Baseband signal has unlimited bandwidth.
  Spectrum of pass-band signal is shifted from baseband signal.
  Thus, pass-band signal has unlimited bandwidth.
  In wireless channel, only limited bandwidth resource is available!
  We want to choose a non-rectangular pulse shape that is limited in
bandwidth!
Baseband
Modulation
Pulse shaping
Frequency Upconversion

## Slide 162: PULSE SHAPING
41
Nyquist criterion
– Design the overall response of Tx filter and Rx filter,
such that
p(0)  1 , and
Tx filter
Rx filter
Channel
Sampling rate Ts
Continuous time waveform
Discrete time samples
p(nTs )  1 n  0
-1
– Avoid one symbol interferes with other symbols (Intersymbol interference)
1 1
pT (t)  1
pR (t)  1
p(t)  pT (t)  pR (t)

## Slide 163: PULSE SHAPING
42
-1
1
1
Waveform at Rx
1
1

## Slide 164: PULSE SHAPING
43
Raised cosine (RC) pulse
 
s
s
1  
2T
sin  cos 
T T
p(t)   s    s 
 4t 2
 t 
t T
 t 
Frequency (Rs)
 / 2
BW  (1 )Rs
PRC ( f )
Time (Ts)
Satisfy Nyquist criterion
 :
Roll-off factor

## Slide 165
44
PULSE SHAPING
Root raised cosine (RRC) pulse
– The frequency domain response of RRC filter is the square root of the
frequency response of RC filter
PRRC ( f )  PRC ( f )
Channel
PRRC ( f )
PRRC ( f )
– RRC filter has the same bandwidth as RC filter
The overall response is RC filter
– Satisfy Nyquist criterion
PRC ( f )  PRC ( f )
PRC ( f ) 
Poverall( f ) 
x(n)
xˆ(n)

## Slide 166
45
PULSE SHAPING
Root Raised Cosine (RRC)
2 2 2
cos
s
s
s
s
s
 T   t R 
tR (4tR )
116
(1 )
tR  sin
(1  )
p(t)  4
1
RRC filter is used at both Tx and Rx
  Overall response is Raised Cosine
  Signal bandwidth is (1  )Rs
Symbol rate:
Signal bandwidth is proportional to symbol rate
Rs  1/ Ts

## Slide 167: OUTLINE
46
Modulation
Linear Modulation Techniques I
Complex Signal Representation
Pulse Shaping
Linear Modulation Techniques II
Non-linear modulation
FDMA

## Slide 168: LINEAR MODULATION II: 16-QAM
47
16 Quadrature amplitude modulation (16QAM)
  Inphase: 4 amplitude shift keying
  Quadrature: 4 amplitude shift keying
s(t)  sI (t) cos(2fct)  sQ (t) sin(2fct)
s (t) {3,1,1,3}
I
16-QAM symbols
sQ (t) {3,1,1,3}
~s (t)  s (t)  j  s (t)
I Q
Total 4 x 4 = 16 possible combinations.
M = 16  bits/sym
Gray mapping
Two adjacent symbols differ only in 1 bit
The most common error is that the receiver decide in favor of the neighbor of the correct symbol.
  With Gray mapping, only 1 bit error.
2
log M  4
 |  | Im | 
0010 | 0110 | 1110 | 1010
0011 | 0111 | 1111 | 1011
0001 | 0101 | 1101 | 1001
0000 | 0100 | 1100 | 1000
Re

## Slide 169: LINEAR MODULATION II: OQPSK
48
Offset quadrature phase shift keying (OQPSK)
– Motivation:
information in amplitude  high requirement in amplifier
 increase error in wireless communication systems.
We want to avoid phase change of
– Avoid two bits (inphase, quadrature) change at the same time !
– OQPSK: Delay the quadrature component by half symbol period such that the
inphase bit and quadrature bit don’t change at the same time.
(00)
(01)
(11)
(10)

QPSK (  / 4 , 3 / 4 , 5 / 4 , 7 / 4 )
00 10 01 11   / 4 , 7 / 4 , 3 / 4 , 5 / 4
Rapid phase change ( e.g. 7 / 4  3 / 4 ) could result in amplitude fluctuation  carries

## Slide 170: LINEAR MODULATOIN II: OQPSK
49
QPSK
OQPSK
OQPSK
  Delay the quadrature component by half symbol period
    It’s guaranteed at any moment, only one bit is changing
    The phase shift of  is completely avoided!
~s (t)  s (t)  j  s (t T / 2)
I Q s
  Disadvantage: phase change every Ts/2  larger bandwidth
BPSK
BPSK
Delay Ts/2
 j

## Slide 171
50
M = 4: QPSK.
LINEAR MODULATION II: MPSK
Multi-ary Phase Shift Keying (MPSK)
– Phase modulation: use phase to carry information.


 







 j 7  
 j 3   j 5 
~s (t)   E exp  j  
Es exp  4 ,
4 , Es exp  4 , Es exp  4 ,
s
m(t) 0,1,, M 1
M = 8: 8PSK.
– 3 bits/sym

0  0


 0 
M
~s (t)  E exp  j2 m(t)  
s
QPSK
8PSK
000
001
010
011
100
101
110
111
4
0
   m(t) 0,1,2,3

## Slide 172: LINEAR MODULATION II: MPSK
51
MPSK demodulation
– Find the modulation symbol that has the smallest Euclidean
distance with the received signal.
000
001
010
011
100
101
110
111
 
8

8

## Slide 173: LINEAR MODULATION II: MPSK
52
Tradeoff between spectral efficiency and energy efficiency
  Spectral efficiency: data rate that is accommodated in unit bandwidth
(bps/Hz) = data rate/bandwidth
    Given fixed bandwidth  fixed symbol rate
    Large M  large # bits/sym  large data rate  large spectral efficiency
  Energy efficiency: at given noise level, how much signal power is required to achieve a certain bit error rate.
    Measured as the value of Eb/N0 required for certain bit error rate (BER).
    Given fixed bandwidth  fixed symbol rate
    Large M  constellation symbols are more “dense”  more sensitive to noise  low energy efficiency
Increase modulation level M  Increase spectral efficiency
Increase modulation level M  Decrease energy efficiency

## Slide 174: OUTLINE
53
Modulation
Linear Modulation Techniques I
Pulse Shaping
Complex Signal Representation
Linear Modulation Techniques II
Non-linear modulation
FDMA

## Slide 175
54
NON-LINEAR MODULATION: FREQUENCY MODULATION
Frequency modulation (FM)
  The term, FM, is usually used when m(t) is analog
    E.g. FM radio
  Use frequency to carry information
f (t)  fc  k f m(t)
  Relationship between phase and frequency
Fixed frequency
Variable frequency
– FM
 (t)  2fct 
2 dt
f (t)  1 d (t)

 (t) 
t
0
2 f (t)dt

t
m(t)dt
0
f
c
 (t)  2f t  k

## Slide 176
55
NON-LINEAR MODULATION: FREQUENCY MODULATION
FM



f
c
c
0
m(t)dt
t
s(t)  A cos2f t  k

## Slide 177
56
NON-LINEAR MODULATION: FREQUENCY MODULATION
FM bandwidth
  The spectrum of FM is much more complicated than the spectrum of AM
  Pass-band Bandwidth of FM signal can be approximated by Carson’s rule.
BT  2( 1)Bs
 :modulation index.
Bs :Bandwidth of baseband signal
E.g.
– AMPS,
– Bandwidth: 32 KHz
  3, Bs  4kHz

## Slide 178
57
NON-LINEAR MODULATION: BFSK
Binary frequency shift keying (BFSK)
– Constant envelope
 c c
s(t)  A sin2 ( f
Ac sin2 ( fc  f )t, 0
 f )t, 1
0
1
0
If continuous phase (CP) 
CP FSK 
No abrupt phase change!

## Slide 179
58
NON-LINEAR MODULATION: MSK
Minimum shift keying (MSK)
– A special case of CP BFSK



 







 



4
4 t
t
A sin 2
s(t)  
, 0
 Rs   , 1
c
c
Rs  
c

 c
A sin2  f
 f 
– CP BFSK with
Advantages:
bandwidth much smaller than BPSK/QPSK
Constant envelope
Very popular modulation scheme for mobile radio
Usually used with Gaussian pulse shaping filter
– GMSK (used by GSM)
4
f  Rs

## Slide 180: NON-LINEAR MODULATION: PRACTICAL ISSUE
59
Power amplifier non-linearity
  Power amplifier: amplify signal power before transmission
    To meet the SNR requirement at receiver.
  Amplifier categories: Class A, Class B, Class AB, Class C, Class D
    Class A: linear amplifier
      Signals amplitude at the operational range is amplified linearly.
      The information in amplitude is preserved.
      Should be used for amplitude modulation.
      Requires more transmission power  short battery life.
    Class C: non-linear amplifier
      Different amplitude range are amplified by different factors
      The amplitude of the signals is distorted.
      CANNOT be used for amplitude modulated systems. CAN be used for frequency modulated systems.
      Requires less transmission power  longer battery life
    From A to B to C to D, linearity becomes worse.

## Slide 181: OUTLINE
60
Modulation
Linear Modulation Techniques I
Pulse Shaping
Complex Signal Representation
Linear Modulation Techniques II
Non-linear modulation
FDMA

## Slide 182: FDMA
61
Frequency division multiple access (FDMA)
  Available spectrum is divided into a set of frequency bands, and each
frequency band is assigned to a user
FDMA is not FDD
  FDD: frequency division duplex
  The downlink and uplink of one user is using different frequencies.
Example: AMPS
  FDMA
  Analog voice: FM
  Digital control: BFSK (one frequency for ‘0’, one frequency for ‘1’).

## Slide 183: FDMA: ACI
62
Adjacent Channel Interference (ACI)
  Interference from adjacent channels.
  For some modulations (FM, FSK), the modulated signal has unlimited bandwidth.
    The signal in one channel will leak into adjacent channels.
    To reduce ACI, introduce some guard bands between adjacent
channels.
  To improve overall bandwidth efficiency, we want to have as many channel as possible in a limited spectrum.
    Tradeoff between bandwidth efficiency and power efficiency.

## Slide 184: ELEG 5693 Wireless Communications Ch 4. Coding
Department of Electrical Engineering
University of Arkansas
Dr. Jingxian Wu
wuj@uark.edu

## Slide 185: OUTLINE
2
Introduction
Source Coding
Channel Coding: Convolutional Code
Interleaving

## Slide 186: INTRODUCTION
3
Coding
  Source coding
    Convert analog information into digital representation
    Reduce the redundancy in the digital signal (compression)
  Channel coding
    Protect the information from channel distortions by adding
redundancy.
    Cyclic Redundancy Check (CRC), Linear Block Code, Convolutional Code (CC), Turbo Code, Low Density Parity Check (LDPC), etc.
Coding can only be used in digital communication systems.
Source
Coding
Channel Coding
Analog or digital information

## Slide 187: OUTLINE
4
Introduction
Source Coding
Channel Coding: Linear Block Code
Channel Coding: Convolutional Code
Interleaving

## Slide 188: SOURCE CODE
5
Why source code?
  Convert analog signal into digital signal
    Sampling and quantization, speech coding.
  Reduce redundancy in digital signal representation (compression)
    To save bandwidth  improve bandwidth efficiency.
    E.g. Winzip
Source code can be classified into two categories
  Lossless source code
    No information is lost during compression
    The original information can be perfectly recovered from the
compressed information.
  Source code with loss
    Some information is lost during compression
    The original information cannot be perfectly recovered after compression.
    Analog to digital conversion, JPEG, MPEG.

## Slide 189: SOURCE CODE: SAMPLING
6
Sampling and quantization
  Convert analog information bearing signal to digital signal without
significant loss of information.
Sampling theorem
  A band-limited signal with highest frequency W Hertz can be completely recovered from its samples if the sampling rate Fs is higher than 2W Hertz.
    Sampling in time-domain  repetition in frequency domain.
f
W
-W
f
W
-W
f
W
Fs
-Fs
Fs
-Fs -W
Fs > 2W
Fs < 2W

## Slide 190: SOURCE CODE: PCM
7
Pulse Code Modulation (PCM): sampling and quantization
  Sampling: 8000 Samples/second (125 us/sample)
    Bandwidth of speech signal in telephone system: 4KHz.
  Quantization: represent each sample by 8-bit sequence (256 discrete levels)
  Data rate: 8000 x 8 = 64 kbps
Sampling
Quantization
64kbps used in wired telephone system: too high for wireless communication!

## Slide 191: SOURCE CODE: ENTROPY
8
There is redundancy in the representation of information.
  Wirxlxss Commuxication (21 characters)
  For efficient information transmission, we want reduce the redundancy
  Given random data sequence, what is the maximum redundancy in the sequence?
    OR: what is the minimum # of bits that can be used to represent the original data without loss of information at receiver?
    OR: what is the maximum compression rate?
Entropy
  Entropy: the minimum # of bits required to represent one symbol from an information source
K
H   pk log2 (1/ pk )
k 0
– K: total # of possible symbols (e.g. 26 English characters) –
: the probability that the k-th character is generated by the source.
pk
(bit/sym)

## Slide 192: SOURCE CODE: ENTROPY
9
E.g. 1: two symbols: ‘0’, ‘1’
– p0 = 0.5, p1 = 0.5
H =
If there are 100 binary symbols, it can be represented with
bits.
E.g. 2: two symbols: ‘0’, ‘1’
– p0 = 0.9, p1 = 0.1
H =
If there are 100 symbols, they can be represented with
bits.
E.g. 3: two symbols: ‘0’, ‘1’
– p0 = 0, p1 = 1
H =
If there are 100 symbols, they can be represented with
bits.
E.g. 4: the entropy of English is 1.1 ~ 1.6
bits/character
26 characters log2(26) = 4.7 bits
Approximately 2/3 are redundant
If there are 100 English characters, they can be represented by 160 bits
  Against: 470 bits

## Slide 193: SOURCE CODE: SPEECH CODING
10
Speech coding
  Convert analog speech signal into digital signal.
  To reduce the bit rate R as much as possible.
    R   BW   more users in limited spectrum
    R   voice quality  (in general)
  Tradeoff between bandwidth efficiency and voice quality.

## Slide 194: SOURCE CODE: SPEECH CODING
11
Two basic speech coding schemes
  Waveform coders:
    Strive to reproduce time or frequency domain signal waveform as
precisely as possible.
    Source independent
    Moderate complexity and data rates (30 ~ 50 kbps)
    e.g. PCM. Usually used in wired telephone system.
  Vocoders (also called “source code”)
    Analyze & extract key parameters using a priori knowledge of speech characteristics
      Extract speech model parameters
      Synthesize voice in Rx using model parameters
    Signal specific parameters  depends on user and is less robust
    Produces very low data rates (~ 515 kbps)
      Very complex & computationally intensive
    Cellular & PCS applications where minimizing user BW  more users supported in finite spectrum  more $$

## Slide 195: SOURCE CODE: SPEECH CODING
12
Vocoders
  Model the speech generation process of vocal tract of human
  Parameters of speech
    Voice pitch  difficult to extract, usually < 300 Hz
    Pole frequencies  resonant frequencies of vocal tract – Centered around: 500, 1500, 2500, 3500
    Pole amplitudes  relative strength at different pole frequencies
    Speech type  voiced or unvoiced
      Voiced: “m”, “n”, “v”  voice chord vibrations
      Unvoiced: “f”, “s”  air flow through constriction
  These parameters are transmitted by the sender
    Rx uses these parameters to synthesize the human speech
  Very complicated, but low data rate: 5 ~ 13 kbps
  Source dependent
    Suitable for human speech, but not suitable to other sound (e.g. music)

## Slide 196: SOURCE CODE: SPEECH CODING
13
Linear Predictive Coders (LPC)
  A kind of time-domain vocoder
    Extract the time domain parameters of signal.
    Transmit the parameters of the signal instead of the actual waveform.
  Linear predictive: predict the future value based on current values.
    Time domain speech waveform: x  [x1, x2 ,, xN ]
    The current values and future values are correlated!
T
N
a x  a x
N 1  n n n1
xˆ 
The coefficients a are calculated at Tx based on the statistical properties of x.
  x is a random process.
Instead of transmitting x, transmit a!
How to calculate the coefficients? – choose a to minimize the mean square
error (MSE).
a  [a , a ,, a ]T
1 2 N
x  [x , x ,, x ]T
1 2 N

## Slide 197: OUTLINE
14
Introduction
Source Coding
Channel Coding: Convolutional Code
Interleaving

## Slide 198: CHANNEL CODING: OVERVIEW
15
Channel coding
  Protect the transmitted information by adding redundancy.
  E.g. repetition code:
    ‘0’: ‘000’
    ‘1’: ‘111’
Error detection
  Include only enough redundant information such that the Rx can detect an error
by looking at the Rx data.
    E.g. repeat ‘1’ 2 times. Tx (1 1), Rx (0 1)  Receiver knows there is an error, but couldn’t guess what is transmitted
    Send back Negative Acknowledgement (automatic-repeat request: ARQ)
Error correction
  Include enough redundant information such that the Rx can recover the original information by looking at the Rx data.
    E.g. repeat ‘1’ 3 times. Tx (1 1 1), Rx (0 1 1)  Receiver will guess that (1
1 1) is transmitted  detect ‘1’
    Majority decision rule  minimize the probability of error.

## Slide 199: CHANNEL CODING: CHANNEL CAPACITY
16
For an AWGN channel with bandwidth B, the maximum data rate that can be supported by the channel is
C(bps)  B log2 (1 SNR)
Shannon’s coding theorem
– For a channel with capacity C bps and an information source generates information at a rate less than C, then there exists a channel coding technique such that the output of the source can be transmitted by the channel with arbitrarily low error rate.
Source
H < C
Channel coding
Channel Capacity C

## Slide 200: CHANNEL CODING: LBC
17
Linear block code (LBC)
  Every k bits of information corresponds to a codeword of length n bits
    E.g. repetitionon code 1-bit of information, 3-bit codeword
  n > k: there are (n-k) bits of redundancy
  The code is called: (n, k) linear block code
  Definition: code rate = (information block length)/(codeword length)
    r = k/n
    Measures the efficiency of the code (1-r: the percentage of redundancy)
    E.g.: (3, 1) repetition code: r = 1/3. (2, 1) repetition code: r = 1/2.
LBC
k bits information
n bits codeword

## Slide 201: CONVOLUTIONAL CODING
18
What is convolutional code (CC)
  n-bit codeword depends on not only current input, but also previous input
    The encoder has memory
  linear block code: n-bit codeword determined uniquely by the k-bit information
  Compared to linear block code
    Can achieve larger dmin with higher coding rate.
– Better power efficiency with larger bandwidth efficiency
    More complex than LBC
Parameters
  (n, k, K)
  Every k-bit input leads to n-bit output
    Coding rate r = k/n
  K: constraint length (related to memory depth of the encoder)

## Slide 202: CC: ENCODER
19
Register representation
m: current 1-bit input.
r1, r2, r3: contents in shift register. Depends on current input and previous input
  r1 = m: current input
  r2, r3: previous inputs
c1 and c2: 2-bit output. Depends on r1, r2, r3
  c1 = r1 + r2 + r3
  c2 = r1 + r3
– (n = 2, k = 1, K = 3)
m
c1
c2
r1 |  | r2 | r3 | 

## Slide 203: CC: ENCODER
20
Example: m = [1 1 0 0], initially (r1=0, r2=0, r3=0)
1 |  | 0 | 0 | 
1
1+0+0=1
1+0=1
first input bit: 1
1 |  | 1 | 0 | 
1
1+1+0=0
1+0=1
second input bit: 1 (shift 1 bit to the right)
0 |  | 1 | 1 | 
0
1+0+0=1
0+1=1
third input bit: 1
(shift 1 bit to the right)
0 |  | 0 | 1 | 
0
1+0+0=1
0+1=1
fourth input bit: 1 (shift 1 bit to the right)

## Slide 204: CC: ENCODER
21
State
  Every input depends on current input r1=m, and previous inputs (r2, r3)
  State: (r2, r3): state a: 00; state b: 10; state c: 01; state d: 11
Input-output table representation
Input | Current state (r2, r3) now | (r1, r2, r3) | Next state (r2, r3) after shift | Output (c1, c2)
0 | a (0 0) | 0 0 0 | a ( 0 0) | (0, 0)
0 | c (0 1) | 0 0 1 | a (0 0) | (1, 1)
0 | b (1 0) |  |  | 
0 | d (1 1) |  |  | 
1 | a (0 0) |  |  | 
1 | c (0 1) |  |  | 
1 | b (1 0) |  |  | 
1 | d (1 1) |  |  | 

## Slide 205
22
CC: ENCODER
(n, k, K)
  n = 2: 2-bit of output
  k = 1: 1-bit of input
  K = 3: output depends on current input, and two previous inputs
State:
  Every output depends not only current input, but also (K – 1) = 2 previous inputs  the encoder remembers the previous (K – 1) inputs  the encoder has a memory depth of (K-1)
  For a particular 1-bit of input, the encoder might be in one of 4
possible states  there are four possible outputs
  Output depends on:
    1. current input
    2. state of the encoder
– # of states:
2( K 1)k

## Slide 206: CC: ENCODER
23
State transition representation
– (2, 1, 3)-CC, 2( K 1)k
a: 00
b: 10
c: 01
d: 11
a=00
b=10
d=11
c=01
 4 states
0/00
1/11
1/01
1/10
0/01
0/10
1/00
0/11
input/output
: input 0
: input 1

## Slide 207: CC: ENCODER
24
Example: encoding by using state transition diagram
  Initial state: a
  Input bits: (1 1 0 0 0 1 0)
  1st bit: (state = a, input = 1)  (next state = b, output = 11)
  2nd bit: (state = b, input = 1)  (next state = d, output = 01)
  3rd bit: (state = d, input = 0)  (next state = c, output = 01)
  4th bit: (state = c, input = 0)  (next state = a, output = 11)
  5th bit: (state = a, input = 0) 
  6th bit:
  7th bit:

## Slide 208: CC: ENCODER
25
Trellis diagram representation
a: 00
b: 10
c: 01
d: 11
input/output
a = 00
b = 10
d = 11
c = 01
0/00
0/00 1/11
1/11
0/10
1/01
0/00
1/11
0/10
1/01
0/01
1/10
0/11
1/00

## Slide 209: CC: ENCODER
26
Example:
  initial state: a
  Input bits: (1 1 0 0 0 1 0)
  1st bit: (state = a, input = 1)  (next state = b, output = 11)
  2nd bit: (state = b, input = 1) 
  3rd bit:
  4th bit:
  5th bit:
  6th bit:
  7th bit:
1/11
0/10
1/01
0/01
1/10
0/11
1/00
a 0/00
b
c
d

## Slide 210: CC: ENCODER
27
Four alternative encoder representations:
  Register representation
    Usually used by hardware implementation of CC encoder
  Input-output table representation
  State transition diagram representation
  Trellis diagram representation
    Mainly used by decoder for decoding
  The 4 alternative representations are equivalent
    Given one representation, we can easily find out the other three representations.

## Slide 211: CC: DECODER
28
Optimum hard decoding
CC
Encoder
Channel
Demodulator
CC
Decoder
Modulator
s c x
y
cˆ
sˆ
s: length m information vector (sequence of 0’s and 1’s)
c: length n = m/r CC codeword (sequence of 0’s and 1’s)
x: modulated symbols (modulation symbols)
y: received symbols (distorted by channels)
cˆ: length n = m/r demodulated information (sequence of 0’s and 1’s)
sˆ: decoded length r information vector (sequence of 0’s and 1’s).
If the block length is m, there are 2m possible codewords
  Decoding: find the codeword that has the smallest Hamming
distance with cˆ

## Slide 212: CC: DECODER
29
Example: block length m = 3, initial state a (0 0)
– Input (0 0 0)  output (0 0 0 0 0 0)
– Input (0 0 1)  output (0 0 0 0 1 1)
– Input (0 1 0)  output (0 0 1 1 1 0)
– Input (0 1 1)  output (0 0 1 1 0 1)
– Input (1 0 0)  output (1 1 1 0 1 1)
– Input (1 0 1)  output (1 1 1 0 0 0)
– Input (1 1 0)  output (1 1 0 1 0 1)
– Input (1 1 1)  output (1 1 0 1 1 0)
– If the vector after demodulator is
Distance with the 8 possible codewords
– c1: 3, c2: 3, c3: 4, c4:
Winner:
Decoded information:
cˆ  [1 0 0 1 0 1]
, c5: , c6: , c7:
, c8:

## Slide 213: CC: DECODER
30
Optimum hard decoding: find the codeword with the smallest Hamming distance
  Exhaustive searching works fine when information block length is small
    m = 3  2^3 = 8 possible codewords
    m = 8  2^8 = 256 possible codewords
  The computational complexity becomes inhibitively expensive when information block length is large
    Typical information block length: 100
m = 20 
m = 100 
When m is large, it’s impossible to find the optimum codeword by exhaustive searching all the possible codewords!
The optimum hard decoding can be performed by exploiting the trellis
structure of the encoder
  Viterbi algorithm
220  1,048,576
2100  1.271030

## Slide 214: CC: DECODER
31
Optimum decoding by using Viterbi algorithm
  The process of CC encoding is equivalent to find a path along the trellis
transition diagram.
    E.g. Input of CC encoder (1 1 0)  codeword: (11 01 01)
  Decoding: find out the path with the smallest Hamming distance with received codeword.
a = 00
b = 10
d = 11
c = 01
0/10
1/01
1/11
0/10
1/01
0/01
1/10
0/00 0/00 0/00 1/11 1/11 0/11
1/00

## Slide 215: CC: DECODER
32
Optimum decoding by using Viterbi algorithm
– At each transition, for each ending state, find the branch minimizing the accumulated Hamming distance (survival branch)
dk  dk 1  d(current output,branch output)
dk 1 : accumulated Hamming distance from the previous transition
d(current output,branch output): the Hamming distance of this branch
0/00
1/11
0/10
1/01
0/11
1/00
0/01
1/10
One survival branch for each ending state!

## Slide 216: CC: DECODER
33
Viterbi algorithm: example (first transition)
a = 00
d = 11
a: d1 = 0+d(10, 00) = 1
c = 01
0/00 (1)
1/11 (1)
b = 10
10
Output of demodulator:
01
01
11
b: d1 = 0+d(10, 11) = 1

## Slide 217: CC: DECODER
34
Viterbi algorithm: example (second transition)
a = 00
b = 10
d = 11
c = 01
0/00 (1)
1/11 (1)
10
Output of demodulator:
01
0/00 (2)
01
11
a: d2 = 1+d(01, 00) = 2
b: d2 = 1+d(01, 11) = 2 c: d2 = 1+d(01, 10) = 3
1/11 (2)
0/10 (3)
1/01 (1)
d: d2 = 1+d(01, 01) = 1

## Slide 218: CC: DECODER
35
Viterbi algorithm: example (third transition)
a = 00
b = 10
c = 01
1/11 (1)
10
0/00 (1)
Output of demodulator:
01
0/00 (3)
11
1/11 (2)
0/10 (3)
1/01 (1)
01
0/00 (2)
0/11 (4)
d = 11
a: d3 = 2+d(01, 00) = 3
d3 = 3+d(01, 11) = 4

## Slide 219: CC: DECODER
36
Viterbi algorithm: example (third transition)
a = 00
b = 10
c = 01
1/11 (1)
10
0/00 (1)
Output of demodulator:
01
0/00 (3)
11
1/11 (2)
0/10 (3)
1/01 (1)
01
0/00 (2)
d = 11
a: d3 = 2+d(01, 00) = 3
d3 = 3+d(01, 11) = 4
1/11 (3)
1/00 (4)
b: d3 = 2+d(01, 11) = 3
d3 = 3+d(01, 00) = 4

## Slide 220: CC: DECODER
37
Viterbi algorithm: example (third transition)
a = 00
b = 10
c = 01
1/11 (1)
10
0/00 (1)
Output of demodulator:
01
0/00 (3)
11
1/11 (2)
0/10 (3)
1/01 (1)
01
0/00 (2)
d = 11
a: d3 = 2+d(01, 00) = 3
d3 = 3+d(01, 11) = 4
1/11 (3)
b: d3 = 2+d(01, 11) = 3
d3 = 3+d(01, 00) = 4
0/10(4)
0/01 (1)
c: d3 = 2+d(01, 10) =
d3 = 1+d(01, 01) =

## Slide 221: CC: DECODER
38
Viterbi algorithm: example (third transition)
a = 00
b = 10
c = 01
1/11 (1)
10
0/00 (1)
Output of demodulator:
01
0/00 (3)
11
1/11 (2)
1/01 (1)
01
0/00 (2)
d = 11
a: d3 = 2+d(01, 00) = 3
d3 = 3+d(01, 11) = 4
1/11 (3)
b: d3 = 2+d(01, 11) = 3
d3 = 3+d(01, 00) = 4
0/10 (3)
1/01(2)
0/01 (1)
1/10 (3)
c: d3 = 2+d(01, 10) =
d3 = 1+d(01, 01) =
d: d3 = 2+d(01, 01) =
d3 = 1+d(01, 10) =

## Slide 222: CC: DECODER
39
Viterbi algorithm: example (fourth transition)
a = 00
b = 10
c = 01
1/11 (1)
10
0/00 (1)
Output of demodulator:
01
0/00 (3)
11
1/11 (2)
1/01 (1)
01
0/00 (2)
d = 11
a: d4 = 3+d(11, 00) = 5
d4 = 1+d(11, 11) = 1
1/11 (3)
0/01 (1)
0/10 (3)
1/01(2)
0/00 (5)
0/11(1)

## Slide 223: CC: DECODER
40
Viterbi algorithm: example (fourth transition)
a = 00
b = 10
c = 01
1/11 (1)
10
0/00 (1)
Output of demodulator:
01
0/00 (3)
11
1/11 (2)
0/10 (3)
1/01 (1)
01
0/00 (2)
d = 11
a: d4 = 3+d(11, 00) = 5
d4 = 1+d(11, 11) = 1
1/11 (3)
0/01 (1)
1/01(2)
0/11(1)
b: d4 = 3+d(11, 11) = 3
d4 = 1+d(11, 00) = 3
1/11 (3)
1/00 (3)

## Slide 224: CC: DECODER
41
Viterbi algorithm: example (fourth transition)
a = 00
b = 10
c = 01
1/11 (1)
10
0/00 (1)
Output of demodulator:
01
0/00 (3)
11
1/11 (2)
0/10 (3)
1/01 (1)
01
0/00 (2)
d = 11
a: d4 = 3+d(11, 00) = 5
d4 = 1+d(11, 11) = 1
1/11 (3)
0/01 (1)
1/01(2)
0/11(1)
b: d4 = 3+d(11, 11) = 3
d4 = 1+d(11, 00) = 3
1/11(3)
c: d4 = 3+d(11, 10) = 4
d4 = 2+d(11, 01) = 3
d: d4 = 3+d(11, 01) = 4
d4 = 2+d(11, 10) = 3
0/01(3)
1/10(3)

## Slide 225: CC: DECODER
42
Viterbi algorithm: example: survival path
a = 00
b = 10
c = 01
1/11 (1)
10
0/00 (1)
Output of demodulator:
01
0/00 (3)
11
1/11 (2)
0/10 (3)
1/01 (1)
01
0/00 (2)
d = 11
a: d4 = 3+d(11, 00) = 5
d4 = 1+d(11, 11) = 1
1/11 (3)
0/01 (1)
1/10 (3)
0/11(1)
b: d4 = 3+d(11, 11) = 3
d4 = 1+d(11, 00) = 3
1/11(3)
0/01 (3)
c: d4 = 3+d(11, 10) = 4
d4 = 3+d(11, 01) = 4
0/10(4)
1/01(2)
1/01 (3)
d: d4 = 3+d(11, 01) = 4
d4 = 3+d(11, 10) = 4

## Slide 226: CC: DECODER
43
Viterbi algorithm: example: survival path
a = 00
b = 10
d = 11
c = 01
1/11 (1)
10
0/00 (1)
Output of demodulator:
01
0/00 (3)
11
1/11 (2)
0/10 (3)
1/01 (1)
01
0/00 (2)
1/11 (3)
0/01 (1)
1/10 (3)
0/11(1)
1/11(3)
0/01 (3)
1/01 (3)
0/10(4)
1/01(2)
Output of decoder: 1 1 0 0

## Slide 227: OUTLINE
44
Introduction
Source Coding
Channel Coding: Linear Block Code
Channel Coding: Convolutional Code
Interleaving

## Slide 228: INTERLEAVING
45
Motivation
  In fading channel, error usually occurs in burst:
    a sequence of consecutive error bits.
  Some channel coding scheme can only correct a few bits of error in one block
    E.g. (5, 2) linear block code can correct only 1 bit error in one block.
  What if the number of error bits in one block exceeds the correction ability of the channel code?
  Solution: interleaving!
Interleaving
  Spread out bits of one codeword in time such they are undergoing independent fading.
  Two kinds of interleaver:
    block interleaving
    Convolutional interleaving.

## Slide 229: INTERLEAVING
46
Block interleaving
  Spread the encoded data into a rectangular matrix of m row and n
columns.
  The matrix is filled row-wise
•
– The matrix is readout column-wise
b1  (1,1),b2  (1,2),, bn  (1, n) bn1  (2,1),, b2n  (2, n)
Channel
coding
Interleaving
Modulation
Channel
demodulation
Deinterleaving
Channel
Decoding

## Slide 230: INTERLEAVING
47
Block interleaving
– E.g. before interleaving: [b1, b2, b3, b4, b5, …, b11, b12]
After interleaving
– [b1, b5, b9, b2, b6, b10, b3, b7, b11, b4, b8, b12]
  The bits are transmitted in this order
  One codeword is spread out in time
Block deinterleaving
  At the receiver, the deinterlever performs the reverse operation
    Fill the matrix with the received bits column wise
    Read out the matrix row wise.
b1 | b2 | b3 | b4
b5 | b6 | b7 | b8
b9 | b10 | b11 | b12

## Slide 231: INTERLEAVING
48
How could interleaving help?
  E.g. if 3-bit burst error happens during transmission
    [b1, b5, b9, b2, b6, b10, b3, b7, b11, b4, b8, b12]
  After deinterleaving
    [b1, b2, b3, b4, b5, b6, b7, b8, b9, b10, b11, b12]
– the 3-bit error is spread out to three codewords!
  The system can correct 3-bit error !
b1 | b2 | b3 | b4
b5 | b6 | b7 | b8
b9 | b10 | b11 | b12

## Slide 232: INTERLEAVING
49
Block interleaving
  The burst of m consecutive errors results in isolated 1-bit error at
the output of the deinterleaver
  The number of rows m is called the interleaver depth
    The correction capability of channel coding is multiplied by m
times!
  Cost:
    longer delay:
      decoding cannot be performed until all mn bits are received. (delay improved by a factor of m)
      Tradeoff between power efficiency and delay
    Larger memory
      mn bits
      (without interleaver: n bits)

## Slide 233: SUMMARY
50
Source coding
  Why? Convert analog information into digital; reduce redundancy.
  Lossless source code, source code with loss.
  PCM, Entropy, speech coding (waveform, vocoder)
Channel coding
  Add redundancy to protect information (error correction, error detection) 
tradeoff between bandwidth efficiency and power efficiency
  Channel capacity
Linear block code
  Generation matrix, parity check matrix, syndrome decoding
  Coding rate, Hamming distance, Minimum Hamming distance
Convolutional code
  Four representations (shift register, input-output table, state transition, trellis)
  Decoding: Viterbi algorithm
Interleaving
  Spread out the bits of one codeword in time
  Block interleaver.
  Tradeoff between power efficiency and processing delay.

## Slide 234
Department of Electrical Engineering
University of Arkansas
ELEG 5693 Wireless Communications
Ch. 5 Equalization
Dr. Jingxian Wu
wuj@uark.edu

## Slide 235: OUTLINE
2
Introduction
Maximum Likelihood Sequence Estimation (MLSE)

## Slide 236
3
INTRODUCTION
Frequency selective fading
  Frequency domain: Signal bandwidth >> channel coherence bandwidth
  Time domain: symbol period << rms delay spread
    Relative arrival time of the multipath components is no longer negligible!
L
h(t, )  hl (t)  ( l )
l 1
The relative power and delay of the multipath component.
E.g.
t: time variation,  : relative delay between multipath component.
– Power delay profile:
0
Ts t
0.5 0.5
If the first multipath component arrives at receiver at time 0, then the second
multipath component arrives at receiver at time Ts.

## Slide 237: INTRODUCTION: ISI
4
Intersymbol interference (ISI)
– E.g. two resolvable multipath components with relative delay Ts.
1st multipath component:
2nd multipath component:
– Tx symbol:
x1, x2 , x3 ,, xk , xk 1,
– In the channel
the 1st multipath:
the 2nd multipath:
0 1 0 2 0 3
h (1)x , h (2)x , h (3)x ,
h0 (1), h0 (2), h0 (3),, h0 (k), h0 (k 1),
h1 (1), h1 (2), h1 (3),, h1 (k ), h1 (k 1),
0, h1(2)x1, h1(3)x2 , h1(4)x3 ,,
– Rx symbols are the combination of the two multipath components
y1  h0 (1)x1  0  n1
2 0 2 1 1 2
y  h (2)x  h (2)x  n
y3  h0 (3)x3  h1(3)x2  n3 yk  h0 (k)xk  h1(k)xk 1  nk
AWGN

## Slide 238: INTRODUCTION: ISI
5
ISI (Cont’d)
yk  h0 (k)xk  h1(k)xk 1  nk
The received symbol is a combination of two or more information symbols!
  xk : desired symbol. xk 1 : Interference from multipath component.
Intersymbol interference:
  Interference caused by multipath components of frequency selective
fading.
ISI model
– L resolvable multipath components with relative delay Ts.
yk  h0 (k)xk  h1(k)xk 1  hL1(k)xk L1  nk
L1
yk  hl (k)xk l  nk
l 0

## Slide 239: INTRODUCTION: DISCRETE-TIME MODEL
6
What if the relative delay between multipath component is not an integer multiply of symbol period Ts ?
– Discrete-time model can convert the channel impulse response into desired form
Discrete-time model
pT (t)
pR (t)
y(t)
Tc
g(t, )
pulse shaping
fading
receiver filter
Continuous-time System Representation
v(t)
Discrete-time Input
Discrete-time Output
Statistical Continuous-time System Representation
Can we replace the continuous-time system with an equivalent discrete-time system
without changing system input-output relationship?
k
x
k
y

## Slide 240: INTRODUCTION: DISCRETE-TIME MODEL
7
Composite impulse response
h(t, )  pT ( )  g(t, )  pR ( )

y(t)  x(t)  h(t, )   xk h(t,  kTs )  n(t)
k 


y(mTs )   xk h(mTs , (m  k)Ts )  n(mTs )
k 
– Represent with discrete-time variables
ym   xk hmk (m)  nm
k 
L
ym  hl (m)xk l  nm
l 0
hl (m)  h(mTs ,lTs )
v(t)  pR (t)

– System model
x(t)   xk (t  kTs ),
k 
– After sampling

## Slide 241: INTRODUCTION: EQUALIZATION
8
What is equalization?
  Signal processing operation employed at receiver to mitigate the effects of ISI.
  Adaptive equalization
    Time-varying frequency-selective fading Channel impulse response varies with time
    The equalizer should vary with time as well!  adaptive equalization.
A possible equalization method:
– At time 1, y1  h0 (1)x1  0  n1
(no ISI)  xˆ1  y1 / h0 (1)
At time 2,
At time 3,
y2  h0 (2)x2  h1(2)x1  n2  xˆ2  y2  h1(2)xˆ1 / h0 (1)
 xˆ3  y3  h1(3)xˆ2 / h0 (3)
y3  h0 (3)x3  h1(3)x2  n3
Problem:xˆi1f
is in error, all the remaining symbols will be affected!
Error propagation.

## Slide 242: INTRODUCTION: CLASSIFICATION
9
Classification
  Linear equalization: only linear operations are employed in equalizer.
    Zero Forcing (ZF), least mean square error (LMS), minimum mean
square error (MMSE), etc
    Advantages: simple
    Not commonly used in wireless communication system.
  Non-linear equalization:
    Decision feedback equalization (DFE), Maximum Likelihood Sequence Estimation (MLSE), Delayed Decision Feedback Equalization (DDFE), Reduced State Sequence Estimation (RSSE), Turbo Equalization, ……
    More complex than linear equalization
    Better performance
    Widely used in wireless communication systems.
MLSE is the optimum equalizer
  It has the best performance among all the equalizers
  It has the highest computational complexity.

## Slide 243: OUTLINE
10
Introduction
Maximum Likelihood Sequence Estimation (MLSE)

## Slide 244
11
MLSE
System model
  Symbols are transmitted in block (assume N symbols per block)
x [x1, x2 ,, xN ]
  The kth symbol at receiver
L1
yk  hl (k)xk l  nk
l 0
2 




L1
yk  hl (k)xk l
l 0
1 1
p( yk | x)  p(nk )  2 exp  2
– nk is AWGN with variance
 2 
is Gaussian distributed
L1
l 0
k l k l
y  h (k)x

## Slide 245
12
MLSE
Likelihood function
– White noise  nj is independent of

ni
p(ni , nj )  p(ni ) p(nj )
p( y1, y2 ,, yN | x)  p(n1) p(n2 ) p(nN )
2 


L1
yk  hl (k)xk l
l 0




N
N
2
2
exp 
1
1
  
k 1


k l
 k  l
2 


N L1
k 1 l 0
2
y  h (k)x
1

exp


1
2 N
Maximum Likelihood
– Find
that maximize
– Equivalent to: minimize
x [x1, x2 ,, xN ]
p( y1, y2 ,, yN | x)
2
N L1
J   yk  hl (k)xk l
k 1 l 0

## Slide 246: MLSE: COST FUNCTION
13
Maximum Likelihood Sequence Estimation
– Based on the information of the received symbols
y  [ y1, y2 ,, yN ]
and the channel impulse response, find the sequence that minimizes the following cost function
x [x1, x2 ,, xN ]
N
k k
J   y  r
k 1
2
Most direct way: exhaustive searching
can take one of M
N symbols per block
There are totally possibilities of
If N = 100, M = 8, then we need to search
M-ary modulation
  Modulation constellation size: M  each xk
possible values.
x [x1, x2 ,, xN ]
possibilities
L1

l 0
hl (k)xk l
where rk 

## Slide 247: MLSE: STATE REPRESENTATION
14
xk
xk
xk 1
h0 (k)
h1 (k )
State representation of frequency selective fading
yk  h0 (k)xk  h1(k)xk 1  nk  rk  nk
rk
N
k k
J   y  r
k 1
2
Cost function:
E.g. QPSK
– How many states?
Re
Im
Es
00 (s1)
(s2) 10
11
(s3)
01 (s4)

## Slide 248: MLSE: STATE REPRESENTATION
15
State representation
  E.g. QPSK (four symbols: s1, s2, s3, s4), L = 2
    M^(L-1) = 4 states: a: (s1), b: (s2), c: (s3), d: (s4).
Input | Current state xk 1 now | Register contents | Next state xk 1 after shift
s1 | a (s1) | (s1, s1) | a (s1)
s1 | b (s2) | (s1, s2) | a (s1)
s1 | c (s3) | (s1, s3) | a (s1)
s1 | d (s4) | (s1, s4) | a (s1)
s2 | a (s1) | (s1, s1) | b (s2)
s2 | b (s2) | (s1, s2) | b (s2)
s2 | c (s3) | (s1, s3) | b (s2)
s2 | d (s4) | (s1, s4) | b (s2)

## Slide 249: MLSE: STATE REPRESENTATION
16
State representation
Input | Current state xk 1 now | Register contents | Next state xk 1 after shift
s3 | a (s1) | (s3, s1) | c (s3)
s3 | b (s2) | (s3, s2) | c (s3)
s3 | c (s3) | (s3, s3) | c (s3)
s3 | d (s4) | (s3, s4) | c (s3)
s4 | a (s1) | (s4, s1) | d (s4)
s4 | b (s2) | (s4, s2) | d (s4)
s4 | c (s3) | (s4, s3) | d (s4)
s4 | d (s4) | (s4, s4) | d (s4)

## Slide 250: MLSE: TRELLIS REPRESENTATION
17
s1/(s1,s1)
a (s1)
c (s3)
d (s4)
s2/(s2,s1)
s3/(s3,s1)
b (s2)
s4/(s4,s1)
input/(register contents)

## Slide 251: MLSE: TRELLIS REPRESENTATION
18
Example
– For a BPSK system with channel length three, how many states do
we have? Draw the trellis diagram.

## Slide 252: MLSE: VITERBI ALGORITHM
19
Viterbi algorithm
– Each state transition corresponds to one pair of
E.g. (state a  state c) 
2 2
k k k k 0 k 1 k 1
J  y  r  y  h (k)x  h (k)x
(xk , xk 1)
(xk  s3, xk 1  s1)
Thus, for each state transition, we can calculate
rk  h0 (k)xk  h1(k)xk 1
For each transition, we can find out the Euclidean distance between yk and rk
– Utilizing the trellis diagram, find out the path with the minimum accumulated Euclidean distance
N N
k k k
J   J   y  r
k 1
2
k 1

## Slide 253: MLSE: VITERBI ALGORITHM
20
Example
  BPSK
  Channel
h0 (1) 0.3  0.5 j | h0 (2) 0.4  0.6 j | h0 (3) 0.5  0.7 j
h1 (1) 0.8  0.4 j | h1 (2) 0.7  0.2 j | h1 (3) 0.6  0.3 j
– Rx symbols
y1
0  0.3 j
y2
 0.4 1.3 j
y3
1.7  0.8 j
– Using Viterbi algorithm finding out what are the sending
symbols ?
x1 x2 x3
s1  1
s2  1

## Slide 254: MLSE: VITERBI ALGORITHM
21
s1/(s1,s1)
Trellis diagram
– # of states M^(L-1) = 2^(2-1) = 2
s1/(s1,s1)
s2/(s2,s1)
s2/(s2,s1)
s1/(s1,s2)
s2/(s2,s2)

## Slide 255: MLSE: VITERBI ALGORITHM
22
s2/(s2,s1)
0.3  0.5 j
0.8  0.4 j
0  0.3 j
s1/(s1,s1)
a: (s1, s1)  r1  1 h0 1 h1  1.1 0.9 j
h0 h1 y
0.4  0.6 j
0.7  0.2 j
 0.4 1.3 j
0.5  0.7 j
0.6  0.3 j
1.7  0.8 j
J  y  r 2  0  0.3 j  (1.1 0.9 j) 2  2.65
1 1 1
2.65
b: (s2, s1)  r1  1 h0 1 h1  0.5  0.1 j
J  y  r 2  0.41
1 1 1
0.41

## Slide 256: MLSE: VITERBI ALGORITHM
23
s2/(s2,s1)
0.3  0.5 j
0.8  0.4 j
0  0.3 j
s1/(s1,s1)
h0 h1 y
0.4  0.6 j
0.7  0.2 j
 0.4 1.3 j
0.5  0.7 j
0.6  0.3 j
1.7  0.8 j
2.65
ba:
r1  h0  h1  0.3  0.4 j
J   0.4 1.3 j  (0.3  0.4 j) 2  3.38
aa: (s1, s1)  r1   h0  h1  1.1 0.8 j
J  y  r 2   0.4 1.3 j  (1.1 0.8 j) 2  4.9
0.41
2.65+4.9=7.55
1
1
1
1
0.41+3.38=3.79

## Slide 257: MLSE: VITERBI ALGORITHM
24
s2/(s2,s1)
0.3  0.5 j
0.8  0.4 j
0  0.3 j
s1/(s1,s1)
h0 h1 y
0.4  0.6 j
0.7  0.2 j
 0.4 1.3 j
0.5  0.7 j
0.6  0.3 j
1.7  0.8 j
J  y  r 2   0.4 1.3 j  (0.3  0.4 j) 2  0.82
r1 
ab: (s2, s1)  h0  h1  0.3  0.4 j
2.65
ba:
r1  h0  h1  1.1 0.8 j
J   0.4 1.3 j  (1.1 0.8 j) 2  2.5
0.41
2.65+0.82=3.47
0.41+2.5=2.91
1
1
1
1
3.79

## Slide 258: MLSE: VITERBI ALGORITHM
25
s2/(s2,s1)
0.3  0.5 j
0.8  0.4 j
0  0.3 j
s1/(s1,s1)
ab: (s2, s1) 
h0 h1 y
0.4  0.6 j
0.7  0.2 j
 0.4 1.3 j
0.5  0.7 j
0.6  0.3 j
1.7  0.8 j
3.79+11.08=14.87
r1 
2.65
ba:
r1  h0  h1  0.1 0.4 j
0.41
 h0  h1  1.11.0 j
2.91
J  1.7  0.8 j  (0.1 0.4 j) 2  4
J  y  r  1.7  0.8 j  (1.11.0 j) 2  11.08
2
1
1
1 1
3.79
2.91+4=6.91

## Slide 259: MLSE: VITERBI ALGORITHM
26
s2/(s2,s1)
0.3  0.5 j
0.8  0.4 j
0  0.3 j
s1/(s1,s1)
ab: (s2, s1) 
h0 h1 y
0.4  0.6 j
0.7  0.2 j
 0.4 1.3 j
0.5  0.7 j
0.6  0.3 j
1.7  0.8 j
r1 
2.65
ba:
r1  h0  h1  1.11 j
0.41
h0  h1  0.1 0.4 j
2.91
3.79
6.91
3.79+3.4=7.19
2.91+0.4=3.31
J  1.7  0.8 j  (1.11 j) 2  0.4
J  y  r  1.7  0.8 j  (0.1 0.4 j) 2  3.4
2
1
1
1 1

## Slide 260: MLSE: VITERBI ALGORITHM
27
s2/(s2,s1)
0.3  0.5 j
0.8  0.4 j
0  0.3 j
s1/(s1,s1)
h0 h1 y
0.4  0.6 j
0.7  0.2 j
 0.4 1.3 j
0.5  0.7 j
0.6  0.3 j
1.7  0.8 j
2.65
0.41
2.91
3.79
6.91
3.31

## Slide 261: MLSE: VITERBI ALGORITHM
28
s2/(s2,s1)
0.3  0.5 j
0.8  0.4 j
0  0.3 j
s1/(s1,s1)
h0 h1 y
0.4  0.6 j
0.7  0.2 j
 0.4 1.3 j
0.5  0.7 j
0.6  0.3 j
1.7  0.8 j
2.65
0.41
2.91
3.79
6.91
3.31
1
1
1

## Slide 262: MLSE
29
States
– M = 4, L = 3
  # of states:
– M = 8, L = 2
  # of states:
– M = 8, L = 3
  # of states:
– M = 8, L = 4
  # of states:
# of states = M^(L-1)

## Slide 263
Department of Electrical Engineering
University of Arkansas
ELEG 5693 Wireless Communications
Ch. 6 Diversity
Dr. Jingxian Wu
wuj@uark.edu

## Slide 264: OUTLINE
2
Introduction
Classification
Space Diversity Techniques
Space Time Block Code

## Slide 265: INTRODUCTION
3
What is diversity?
  E.g. Transmit the same signal several times.
    Receiver has multiple copies of the same signal.
    Each copy of the signal undergoes independent fading.
    The probability that all the signals are severely distorted (deeply faded) simultaneously is small.
– Diversity: Transmitting multiple replicas of the same signal at statistically independent fading channel to improve communication quality.
The probability that all the signals are distorted by channel is smaller compared to the non-diversity case.

## Slide 266: INTRODUCTION
4
Diversity can be achieved by utilizing the properties of fading
  So far, all of our discussions treat fading as a pure negative factor to reliable high speed wireless communication.
    Time-varying, frequency-selective
    Degrade system performance
  If properly handled, fading can also benefit system performance!!!
  E.g. Time-varying fading:
    Coherent time
– the time period over which the channel is strongly correlated.
    Transmit the same signal at different time periods with interval larger than coherent time
    Achieve diversity in the time domain  Time diversity
Classifications:
  Time diversity
  frequency diversity
  space diversity.

## Slide 267: OUTLINE
5
Introduction
Classification
Space Diversity Techniques
Space Time Block Code

## Slide 268: CLASSIFICATION: TIME DIVERSITY
6
Time diversity
  Repeatedly transmit the information bearing signal at time spacing that exceeds the coherence time of the channel. (time varying fading)
    Signals undergo statistically independent fading in the time domain.
    If one copy of the signal is deeply faded, it’s likely that the other copies can still be detected by the receiver.
  Using redundancy in the time domain to tradeoff performance
    Tradeoff between bandwidth efficiency and power efficiency!
  Example: channel coding with interleaving
    Channel coding  information + redundancy
    Interleaving  spread out the codeword over time.
    If the interleaving depth is large enough, every bit of the codeword undergoes independent fading
– If one or more bit are in error, while the other bits are right, the information can still be recovered.

## Slide 269: CLASSIFICATION: FREQUENCY DIVERSITY
7
Frequency diversity (multipath diversity)
  Transmitting the same information at different frequency bands with spacing larger than the coherent bandwidth (frequency selective fading)
    Signals at different frequency undergo independent fading
  Explanation from time domain:
    Frequency selective fading  multiple copies of the same signal arrive at the receiver at different time due to multipath fading.
    Multipath components are independent  signals propagating through different path are undergoing independent fading  multipath diversity!
  Frequency selective fading  ISI 
  Frequency selective fading  mulitpath (frequency) diversity 
  Frequency diversity can be achieved by using equalization in frequency selective fading
    After ISI is partially removed, what is remaining is frequency
diversity.

## Slide 270: CLASSIFICATION: SPACE DIVERSITY
8
Space diversity (antenna diversity)
  Multiple antennas are used at transmitter and/or receiver, with spacing between two adjacent antennas being chosen to ensure the independence of fading.
    Most popular diversity technique.
  To ensure independence
    Mobile station: antennas are separated half wavelength or more.
– and
are independent
Base station: antenna spacing need to be several tens of wavelengths.
– and
are independent
BS
h11 h12
h21
h22
MS
h11 h12
h11
h21

## Slide 271: CLASSIFICATION: SPACE DIVERSITY
9
Space diversity classifications
  Receive diversity
    Single transmit antenna, multiple receive antenna
    SIMO (single input multiple output)
  Transmit diversity
    Multiple transmit antenna, single receive antenna
    MISO (multiple input signal output)
  Diversity on both transmitter and receiver
    Multiple transmit antennas, multiple receive antennas
    MIMO (multiple input multiple output)

## Slide 272: OUTLINE
10
Introduction
Classification
Space Diversity Techniques
Space Time Block Code

## Slide 273: SPACE DIVERSITY
11
Instantaneous SNR of non-diversity system
  System model
y  h  x  n
  Signal power
2
2
h  x  h Es
Power of modulation symbol
– Noise power
2 
2
n
E n  
– Instantaneous SNR: (signal power/noise power)
0
2
 h 
 2
  h 2
n
E s
SNR without fading

## Slide 274: SPACE DIVERSITY
12
Instantaneous SNR
– Fading h varies with time  SNR
varies with time

The fluctuation of SNR degrades the performance of wireless communication system
If there is no fading (AWGN only), the SNR is constant
  Space diversity will make the SNR more “flat”

## Slide 275: SPACE DIVERSITY: COMMON TECHNIQUES
13
Common receive diversity techniques
  Selection diversity
  Maximal Ratio Combining (MRC)
  Equal Gain (EG) diversity
Common transmit diversity techniques
  Transmit diversity with feedback
  Space time block code
  Space time trellis code
MIMO
  Space time block code
  Space time trellis code

## Slide 276: SPACE DIVERSITY: RECEIVE DIVERSITY
14
System model for receive diversity
1Tx antennas, N Rx antennas.
The signal at the kth Rx antenna:
System equation in matrix format
The same signal is received by N antennas.
  Each signal undergoes independent fading
 n 
2 
 n1 
   
 y N   h N   n N 
 y   h 
 ⁝ 
 
 ⁝   ⁝ 
2   x  
 2   
 y1   h1 
h N
⁝
Rx 1
Rx N
1
h
yk  hk  x  nk

## Slide 277: SPACE DIVERSITY: SELECTION DIVERSITY
15
Selection diversity
  Out of the N received signals, at each symbol period, choose the one with the maximum instantaneous SNR.
    Demodulation and decoding is performed for the signals with the maximal SNR.
    Signals on other antennas are discarded.
SNR of the kth Rx antenna
2
 k  hk   0
SNR after selection diversity
 max  ,  , ,  
1 2 N
 sel
Logic Circuits
Measure SNR
Measure SNR
⁝
Output r
y N
y1

## Slide 278: SPACE DIVERSITY: SELECTION DIVERSITY
16
SNR after selection diversity (N = 3)
 1
 2
 3
 sel

## Slide 279
17
⁝
 r2    rN
Output r  r1
1
y
1
SPACE DIVERSITY: MAXIMAL RATIO COMBINGING
Maximal Ratio Combining (MRC)
h *

y N
N
h *
The signals from all Rx antennas are processed and combined together
The output on the kth branch
k
k k
k
r  h  x  h  n
*
2
r1
rN
– The output of the MRC receiver
k
N
k
h  n 
k
N

k 1
*
r   h  x 
k 1
2

## Slide 280
18
SPACE DIVERSITY: MRC
SNR of MRC
k
N
k
h  n 
k
N

k 1
*
r   h  x 
k 1
2
– Power of signal component
 E s
N


2


 hk
 k 1
2
– Power of noise
N

k 1
2
N

k 1
*
n
k
2
h   2
k
E
k
h  n 

– SNR
2
N
k n
2
  2
 E s

2 
 N
 hk
 h
k 1
   k 1 
N
k
N
k
0
   h 2     
k 1 k 1
The SNR of MRC equals to the sum of SNRs of individual branches!
– MRC is the optimum diversity receiver (highest SNR among all diversity receivers.)

## Slide 281: SPACE DIVERSITY: MRC
19

## Slide 282
20
SPACE DIVERSITY: EQUAL GAIN COMBINING
Equal gain combining (EGC)
⁝
 r2    rN
Output r  r1
y1
e  j 1

y N
r1
e  j N
–
– The output of the kth branch:
 k
rN
: the phase of hk , i.e.,
e j k
hk  hk
k
r  h  x  e  j k  n
k k
– The output of the Equal Gain receiver
k
N
k
e  n 
k
N

k 1
r   h  x 
k 1
 j

## Slide 283: SPACE DIVERSITY: EQUAL GAIN COMBINING
21
SNR of equal gain combining
  0

2

1 
 
N
 hk
N  k 1 
Comparison of Selection diversity, MRC, and EGC

## Slide 284: OUTLINE
22
Introduction
Classification
Receiver Diversity
Space Time Block Code

## Slide 285: STBC
23
Orthogonal Space Time Block Code
  Proposed by Alamouti in 1998
    “A simple transmit diversity technique for wireless communications”, IEEE Journal on Selected Areas of Communications, vol. 16, 1998.
  Suitable for system with 2 Tx antennas and arbitrary number of receive antennas
  A simple, yet powerful space diversity technique
    It doesn’t require any knowledge of the channel at transmitter.
      ALL transmit diversity techniques before STBC require some knowledge of the channel at the transmitter
      The transmitter can learn the channel state through feedback from receiver  extra bandwidth is used for feedback
  It has been adopted by 3GPP HSDPA (High Speed Downlink Packet Access)

## Slide 286: STBC
24
Structure (2 Tx, 1 Rx)
– Assumption: the channel keeps constant during two consecutive symbol
periods ( t1 and ) .
– At time
on antenna 1.
t 2
, transmit x1 on antenna 1, transmit x2 on antenna 2.
1
x
2
x
2
 x *
1
x *
h11
t 2
time
Space
h21
t1
t1
2 2
1
– At time t , transmit  x * on antenna 2, transmit x *
y1  h11 x1  h21 x2  n1
2
y   h x *  h x *  n
2 11 2 21 1

## Slide 287: STBC
25
System equation
11   2   2 
 2   21
*     n * 
x
  x1    n1 
 h
h21
 y *   h *
 y1    h11
y  Hx  n
Channel matrix is orthogonal
H H H 
Receiver
r  H H y 
21 2
21
n *
 | h |2 x  h * n  h
1 11 1
|2
11
1
r  | h
11 2
2 21 1
2 *
21
n *
x  h * n  h
 | h | 
|2
11
2
r  | h

## Slide 288: STBC
26
2 Tx, M Rx
– At time
t1 , transmit
on antenna 1, transmit
on antenna 2.
At the m-th Rx antenna
x1
x2
2
t , transmit
– At time
on antenna 1, transmit
on antenna 2.
At the m-th Rx antenna
*
2
 x
1
x *
y1m
 h1m x1  h2 m x2  n1m
2 m
2 m 1
x *
2
 h x *  n
y 2 m   h1 m
– System equation at the m-th Rx antenna
 2 m   2 m 1 m   2   2 m 
  x   n * 
  x1    n1 m 
 h *
 y *   h *
 y1 m    h1 m h2 m
y m  H m x  n m

## Slide 289: STBC
27
2 Tx, M Rx (Cont’d)
– System equation for all the Rx antennas
     

     x   
⁝ ⁝ ⁝
 n 1
 y 1   H 1 
 y M   H M  n M 
– Receiver
y  Hx  n
r  H H y 

## Slide 290: ELEG 5693 Wireless Communications Ch. 7 Multicarrier Modulation
Department of Electrical Engineering
University of Arkansas
Dr. Jingxian Wu
wuj@uark.edu

## Slide 291: OUTLINE
2
Introduction
OFDM
Challenges in Multicarrier Systems

## Slide 292: INTRODUCTION
3
Multicarrier Modulation (MCM)
  Achieves broadband communication by modulating a large number of
narrow-band data streams over closely spaced sub-carriers.
  Divide a broadband channel into many narrow-band sub-channels in the frequency domain
    Each sub-channel is called a sub-carrier
  Divide the transmitted data stream into many sub-streams, and transmit one sub-stream in one sub-channel
  The data is transmitted over many sub-carrier  multicarrier modulation

## Slide 293: INTRODUCTION
Why MCM?
  Alleviate the impairments caused by inter-symbol interference (ISI)
  Single-carrier broadband communication suffers serious ISI
Time
Multipath 1
Multipath 2
s1 will interfere with s2 and s3  ISI
In MCM, each subcarrier delivers a narrow-band signal
  Narrow-band  longer symbol period
s1 s2 s3 s4 s5 s6 s7 s8
s1 s2 s3 s4 s5 s6 s7
s8
s1
s9
s17
s1
s9
s17
Multipath 1
Multipath 2
Less ISI
ISI can be completely removed by using guard interval between adjacent symbols

## Slide 294: INTRODUCTION
Why MCM (Cont’d)
  Original single-carrier system experiences frequency selective fading
    Data rate >> coherence bandwidth
    Symbol period << rms delay spread
     freqeuncy selective fading
  MCM: on each subcarrier: data rate decreases, the symbol period increases
    data rate << coherence bandwidth
    Symbol period >> rms delay spread
     frequency flat fading
    No equalization is necessary!
5

## Slide 295: INTRODUCTION
MCM techniques
  Orthogonal frequency division multiplexing (OFDM)
    4G cell phone systems
    Most wireless LANs (IEEE 802.11x)
    IEEE802.15 UWB
    Digital audio and video broadcasting
    The most popular MCM technique
  Discrete multitone
    DSL
  Vector coding
  …
6

## Slide 296: OUTLINE
7
Introduction
OFDM
Challenges in Multicarrier Systems

## Slide 297: OFDM
Orthogonal Frequency Division Multiplexing (OFDM)
  Orthogonal: the subcarriers are mutually orthogonal  there is no inter-
carrier interference (ICI) among the subcarriers
  The most popular MCM technique
  Can be implemented with fast Fourier transform (FFT) and inverse fast Fourier transform (IFFT)
8

## Slide 298
OFDM: DFT AND IDFT
Review: DFT and IDFT
– discrete Fourier transform (DFT)
– Inverse discrete Fourier transform (IDFT)
– Linear convolution
– Circular convolution
9
N 1
n0
N
X [i]  1 
x[n]e j 2ni/ N
N 1
i0
N
x[n]  1 
X [i]e j 2ni/ N

y[n]  x[n] h[n]  h[k]x[n  k]
k 
N 1
y[n]  x[n]  h[n]  h[k]x[n  k]N
k 0
N
[k]  k modulo N

## Slide 299: OFDM: DFT AND IDFT
Linear convolution v.s. circular convolution
– Linear convolution
h[0], h[1], h[2], h[3]
x[3], x[2], x[1], x[0]
10
y[0]  h[0]x[0]

y[n]  x[n] h[n]  h[k]x[n  k]
k 
x[3], x[2], x[1], x[0]
y[1]  h[0]x[1]  h[1]x[0]
x[3], x[2], x[1], x[0]
y[2]  h[0]x[2]  h[1]x[1]  h[2]x[0]
x[3], x[2], x[1], x[0]
y[3]  h[0]x[3]  h[1]x[2]  h[2]x[1]  h[3]x[0]
– circular convolution
h[0], h[1], h[2], h[3]
x[0], x[3], x[2], x[1]
N 1
y[n]  x[n]  h[n]  h[k]x[n  k]N
k 0
y[0]  h[0]x[0]  h[1]x[3]  h[2]x[2]  h[3]x[1]
y[1]  h[0]x[1]  h[1]x[0]  h[2]x[3]  h[3]x[2]
y[2]  h[0]x[2]  h[1]x[1]  h[2]x[0]  h[3]x[3]
y[3]  h[0]x[3]  h[1]x[2]  h[2]x[1]  h[3]x[0]
x[1], x[0], x[3], x[2]
x[2], x[1], x[0], x[3]
x[3], x[2], x[1], x[0]

## Slide 300: OFDM: DFT AND IDFT
11
DFT and Circular Convolution
– Circular convolution in the time domain  multiplication in the frequency
domain
DFTy[n]  x[n] h[n] X[i]H[i]
– Circular convolution is preferred in discrete time implementation
– However, practical system has the effect of linear convolution.

## Slide 301: OFDM: CYCLIC PREFIX
Linear convolution
Can we convert linear convolution to circular convolution?
Discrete-time model of a system with frequency selective fading
y[n]  h(k)x[n  k]  z[n]
12
k 0

h[0], h[1], h[2], h[3] x[3], x[2], x[1], x[0], x[3], x[2], x[1]
x[3], x[2], x[1], x[0], x[3], x[2], x[1]
x[3], x[2], x[1], x[0], x[3], x[2], x[1]
x[3], x[2], x[1], x[0], x[3], x[2], x[1]
h[0], h[1], h[2], h[3]
x[0], x[3], x[2], x[1]
x[1], x[0], x[3], x[2]
x[2], x[1], x[0], x[3]
x[3], x[2], x[1], x[0]
– Linear convolution between
and
h[0], h[1], h[2], h[3]
x[1], x[2], x[3], x[0], x[1], x[2], x[3]
– Circular convolution between
and
h[0], h[1], h[2], h[3]
x[0], x[1], x[2], x[3]
x[1], x[2], x[3], x[0], x[1], x[2], x[3]
circular prefix

## Slide 302: OFDM: CYCLIC PREFIX
Cyclic prefix
– Circular convolution between h (length:   1 ) and x can be achieved if
1. Add circular prefix to x, get
2. Perform linear convolution between h and ~x
13
~x
x  x[0], x[1],, x[N 1]
~x  x[N  ],, x[N 1], x[0], x[1],, x[N 1]
 cyclic prefix
N data
 
y[n]  h[k]~x[n  k]  h[k]xn  kN  h[n]  x[n]
k 0 k 0
In a practical system, we can
  1. Add circular prefix to the data
  2. Transmit the cyclic-prefixed data
  3. The channel functions like a linear convolution
  4. At the receiver, remove cyclic prefix, we get a circular convolution.

## Slide 303: OFDM: TRANSMITTER
OFDM Transmitter
14
R
– Modulated data:
X  X [0], X [1],, X [N 1]
– After IFFT:

N 1
i0
x[n] 
j 2ni / N
X [i]e
1
N
x  x[0], x[1],, x[N 1]
– Add cyclic prefix:
~x  x[N  ],, x[N 1], x[0], x[1],, x[N 1]

## Slide 304: OFDM: RECEIVER
15
Receiver
 
Received data sample:y[n]  h[k]~x[n  k]  z[n]  h[k]xn  kN  z[n]  h[n]  x[n]  z[n]
k 0 k 0
–
– After FFT:
Y [i]  H[i]X [i]  Z[i]
i  0,, N 1
the data symbol transmitted on the i-th sub-carrier
H[i]: the channel coefficient of the i-th sub-carrier
The i-th sub-carrier is equivalently modeled as a flat fading channel without ISI
There is no interference among sub-carriers.
X– [i] :

## Slide 305: OFDM: MATRIX REPRESENTATION
Matrix representation of DFT
– Define: DFT matrix
16









N
N
N
N
N
N
N
N
N
e
e
e
e
 e
N 

e
1
 j 2 ( N 1)( N 1) 
 j 2 ( N 1)1
 j 2 ( N 1)0
 j 2 1N 1
 j 2 11
 j 2 10
 j 2 0( N 1)
 j 2 00  j 2 01
⁝
⁝
⁝
 e
 e
⋱
 e
Q 
N 1
Y [i] 
1
N
 y[n]e
n0
N
 j 2 ni
– DFT
– DFT in matrix format









y[N  1]




e
 e
N 
 






 ⁝ 

Y [N  1]
1
Y [0]
Y [1]
e
e
e
e
N
( N 1)( N 1)
y[0] 
y[1] 

 ⁝ 
N
N
N
N
 j 2 11
N
 j 2 10
N
 e
 e
⋱
 e
 j 2
 j 2 1N 1
 j 2 0( N 1)
N
 j 2 01
N
⁝
⁝
 j 2 ( N 1)1
⁝
 j 2 ( N 1)0
 j 2 00
Y  Q  y

## Slide 306: OFDM: MATRIX REPRESENTATION
Matrix representation of IDFT
– Define: IDFT matrix
17








N
N
N
N
N
N
N
N
N
e
e
e e
 e

N 

e
1
j 2 ( N 1)( N 1) 
j 2 ( N 1)1
j 2 ( N 1)0
j 2 1N 1
j 2 11
j 2 10
j 2 0( N 1)
j 2 00 j 2 01
⁝
⁝
⁝
 e
 e
⋱
 e
QH 
N 1
y[n] 
1
N
Y [i]e
i0
N
j 2 ni
– IDFT
– IDFT in matrix format









Y [N  1]



e
 






 ⁝ 

 y[N  1]
1
y[0]
y[1]
e
e e
e
 e

N 
N
( N 1)( N 1)
Y [0] 
Y [1] 

 ⁝ 
N
N
N
N
N
N
 e
 e
⋱
 e
j 2
j 2 1N 1
j 2 0( N 1)
N
j 2 11
j 2 01
N
⁝
⁝
j 2 ( N 1)1
⁝
j 2 ( N 1)0
j 2 10
j 2 00
y  QH  Y

## Slide 307: OFDM: MATRIX REPRESENTATION
Matrix representation of OFDM
– Transmitter:
Data (frequency domain):
IDFT:
Cyclic prefix:
– Channel (time domain):
18






 
 
 
 
 
   


0 

 
 
 

 




 h[1]
 h[0]
 y[N  1]
h[]
 h[] h[  1] 
h[0]  h[] 
⋱ ⋱ ⋱ ⋱
 h[1] h[0] 0
⁝ ⋱ ⋱ ⋱ ⋱
0 0 h[]  h[1]
 y[0]

 y[1]
 ⁝   ⁝
 
 y[]
z[0]
z[1]
h[0]x[N  1] z[N  1]
h[2]
⁝
z[]
⁝
h[1] x[0]
 x[1]  
⁝  ⁝   ⁝ 
x[] 
⁝
⁝
X
x  Q  X
~x
 z[n]
 
y[n]  h[k]~x[n  k]  z[n]  h[k]xn  kN
k 0 k 0
y  Hx  z
H is a cyclic matrix
– Each row is a cyclic shift of the previous row

## Slide 308: OFDM: MATRIX REPRESENTATION
Matrix representation of OFDM (Cont’d)
Receiver
  Time domain:
19
y  Hx  z
Frequency domain: apply DFT at the received signal
Y  Qy  QHx  Qz  QHQH  X  Z  Λ  X  Z
Proposition
  The frequency domain channel matrix, Λ  QHQH , is a diagonal
matrix, with the i-th diagonal element being
N 1
H[i]  h[n]e j 2ni / N
n0
– Proof:

## Slide 309: OFDM: MATRIX REPRESENTATION
20
Matrix representation of OFDM
– Transmitter:
Data (frequency domain):
IDFT:
Cyclic prefix:
– Receiver:
X
x  Q  X
~x
y  Hx  z
Y  Λ  X  Z
After removal of cyclic prefix:
DFT:
Information on the i-th sub-carrier: Y [i]  H[i]X [i]  Z[i]
IDFT
Cyclic Prefix
Channel
Remove Prefix
DFT
X
x
~x
y
Y

## Slide 310: OFDM: MATRIX REPRESENTATION
Example
– Consider a simple two-tap discrete-time channel with impulse response
H (z)  1 0.9z1
find the matrix representation in time and frequency domain of an OFDM system with N = 8.
21

## Slide 311: MCM: OFDM
22/36
OFDM: frequency domain
– Orthogonal in frequency domain  no inter-carrier interference
(ICI) in static channel.
1
T0
2
T0
3
T0
0
T0
Frequency
s0 s1
s2 s3

## Slide 312: OUTLINE
23
Introduction
OFDM
Challenges in Multicarrier Systems

## Slide 313: CHALLENGES: PAPR
Peak-to-average power ratio (PAPR)
A low PAPR
   the time domain amplitude does not change dramatically
   we can use more efficient non-linear power amplifier
A high PAPR
   there is large variation in the time domain amplitude
   a lot of information is carried in the amplitude
   we have to use linear power amplifier, which usually has low efficiency
24
E[| x(t) |2 ]
max | x(t) |2
PAPR  t

## Slide 314: CHALLENGES: PAPR
Example
– What is the PAPR of a sin wave?
25

## Slide 315: CHALLENGE: PAPR
PAPR in OFDM
– The time domain samples are obtained from IDFT of modulated symbols
Based on central limit theorem, when N is large, then x[n] follows zero- mean Gaussian distribution
The theoretical value of the PAPR is infinity (why?)
In practice, the PAPR increases approximately linearly with N
Large N  large PAPR 
Large N  small overhead due to cyclic prefix 
There are many ways to reduce PAPR in practical system
  Clipping the peak signal
  Special coding techniques
  ……
26

N 1
i0
x[n] 
j 2ni / N
X [i]e
1
N

## Slide 316: CHALLENGE: FREQUENCY AND TIMING OFFSET
Frequency and timing offset
cos(2fct)
Frequency offset:
  Due to the inaccuracy of the carrier frequency oscillator, there might
be a small error in
E.g. if the oscillator is accurate to 1 part per million, then the frequency offset for a 5GHz system is
f  f 106 
c
The frequency offset will degrade the orthogonality among the subcarriers.
27
Matched Filter
fc

## Slide 317: CHALLENGE: FREQUENCY AND TIMING OFFSET
Frequency and timing offset
cos(2fct)
Timing offset
  During the sampling of the time domain signal, there might be a small
offset during the sampling
  If the time offset is large, it will cause both ISI and ICI
  If the time offset is small, it will cause ICI
  Generally speaking, the ICI caused by the timing offset is smaller
than that caused by frequency offset.
28
Matched Filter

## Slide 318: CASE STUDY: IEEE 802.11a
IEEE 802.11a: Wireless LAN standard
  Carrier frequency: 5 GHz
  Total BW: 300 MHz
  Channel BW: 20 MHz
  Number of subcarriers: N = 64
    Data: 48; zeros: 12; pilot: 4
Cyclic prefix:
Subcarrier spacing: 20 MHz/64 = 312.5 kHz
Sample period: Ts = 1/20 MHz = 50 ns
Maximum delay spread that can be handled by the system:
OFDM symbol time:
Code: convolutional code with rates 1/2, 2/3 or 3/4
Modulation: BPSK, QPSK, 16QAM, 64QAM
Minimum data rate:
– Maximum data rate:
29
  16

## Slide 319: CASE STUDY: IEEE 802.11a
Example
– Find the data rate of an 802.11a system with 16QAM and 2/3
convolutional coding.
30

## Slide 320
Department of Electrical Engineering
University of Arkansas
ELEG 5693 Wireless Communications
Ch. 8 CDMA
Dr. Jingxian Wu
wuj@uark.edu

## Slide 321: OUTLINE
2
CDMA Fundamentals
Pseudo-noise sequence
Rake receiver

## Slide 322: FUNDAMENTALS
3
Code Division Multiple Access (CDMA)
  Multiple users share the same channel and transmit at the same time.
  Different codes are used to separate the signals from different users.
  The signal occupies a bandwidth much larger than the minimum bandwidth necessary to send the information.
    Spread Spectrum Technologies.
Classifications
  Direct sequence CDMA (DS-CDMA)
    Also called Direct sequence spread spectrum (DSSS)
    Used in IS-95, WCDMA, cdma2000, IEEE 802.11, etc.
    The most commonly used CDMA technique.
  Frequency hopping CDMA (FH-CDMA)
    Also called Frequency Hopping spread spectrum (FHSS)
    Used in original IEEE 802.11, military applications, etc.

## Slide 323
4

N
i i
a b
i1
1
N
1
N
(a1b1  a2b2  aNbN ) 
a  b 
FUNDAMENTALS
Definitions
  Inner product (correlation between two sequences):
    The inner product of two length N vectors a and b is defined as
a [a1, a2 ,, aN ] b [b1,b2 ,,bN ]
Orthogonal:
  Two vectors are orthogonal if their inner product is 0.
a  b  0  a and b are orthogonal
Example
– a = [1 -1 1 -1], b = [1 1 -1 -1]
For binary vector a (contains either -1 or 1)
N N
n1
N
a  a  1 (1)2  1  N  1
4
a  b  1 1111  0

## Slide 324: FUNDAMENTALS: OPERATION
5
CDMA operations: Transmitter
  Each user is assigned a unique code
    Each bit in the code is called a “chip”
    E.g. user 1, c1  [1,1,1,1,1,1,1,1]
  For each user, the modulation symbol s is further modulated by the code
sequence as
(spreading)
– Symbol period
s ci
E.g. BPSK.
  To transmit BPSK symbol „1‟, signal sent out by the user in one
symbol period is
1 c1  [1,1,1,1,1,1,1,1]
  To transmit BPSK symbol „-1‟, signal sent out by user 1 in one symbol period is
1 c1  [1,1,1,1,1,1,1,1]
At each symbol period, instead of transmitting 1 symbol, N chips are transmitted
  Chip period Tc: time duration of one chip
Ts  N Tc

## Slide 325: FUNDAMNETALS: OPERATIONS
6
CDMA operations: receiver
  Despreading: at receiver, performing inner product between received signal and the code sequence of the user
    Rx signal (after fading compensation)
y  s  c1  n
    After despreading:
y  c1  s  c1  c1  n  c1  s  z
– z  n  c1
Example (Assume no noise)
  The Rx sequence is
y  [1,1,1,1,1,1,1,1]
is the noise component after despreading
•
After despreading:
c1  [1,1,1,1,1,1,1,1]
8
1
y  c  1 (11111111)  1

## Slide 326: FUNDAMENTALS: OPERATIONS
7
User 2:
CDMA operations: multiple access
  Each user is assigned a unique sequence
    Ideally, the sequences of different users are orthogonal to each other.
    E.g user 1: c1  [1,1,1,1,1,1,1,1]
c2  [1,1,1,1,1,1,1,1]
8
1 2
c  c  1 11111111  0
– Signals from multiple users are transmitted at the same time and same
bandwidth.
c1  [1,1,1,1,1,1,1,1]
E.g. user 1 “1”:
User 2 “-1”:  c2  [1,1,1,1,1,1,1,1]
Signal at receiver:
r c1 c2  [0,0,2,2,0,2,0,2]
Detect signals from user 1
c1  r  (0  0  2  2  0  2  0  2) / 8  1
Detect signals from user 2
c2  r  (0  0  2  2  0  2  0  2) / 8  1

## Slide 327
8
FUNDAMENTALS: OPERATIONS
Multiple access (Cont’d): why no interference among users?
c1  r  c1  (c1  c2 )  c1  c1  c1  c2  c1  c1  1
c2  r  c2  (c1  c2 )  c2  c1  c2  c2  c2  c2  1
M
mn
Because the spreading codes are orthogonal with each other, there is no interference among users!
If there are M users
r  sm  cm  n
m1
To detect the signal of the nth user
r  cn  sn (cn  cn )   sm (cm  cn )  n  cn  sn  zn
noise after despreader
To guarantee the orthogonality among users, all the M users must be synchronized.
  All users in system must transmit at exactly the same time!
  This requirement can be lowered by using PN code.

## Slide 328: FUNDAMNETALS: PN CODE
9
PN Code (Pseudo-noise Code)
  Binary sequence with random properties  noise like
  Approximately the same number of 0s and 1s.
  Very low correlation between time-shifted version of same sequence
    Auto-correlation of PN code  noise like!
E.g. [-1, -1, -1, +1, +1, -1, +1], time shift by 1: [+1, -1, -1, -1, +1, +1, -1]
– Inner product: (-1+1+1-1+1-1-1)/7 = -1/7
– Very low cross-correlation between different codes.
(t)
t f
PSD


## Slide 329
10
mn
 sn   Im  zn
mn
FUNDAMNETALS: MAI
Multiple access interference (MAI)
M
In practical CDMA systems
  Users are not perfectly synchronized  codes are time shifted 
codes are no longer orthogonal
  The spreading codes among users are not perfectly orthogonal
MAI: interference among users in CDMA system because the codes among users are not perfectly orthogonal.
r   sm  cm  n
m1
To detect the signal of the nth user
r  cn  sn (cn  cn )   sm (cm  cn )  n  cn
MAI
– Usually: cm  cn  cn  cn  1
2
2
n
m
E  I  E s
mn
therefore

## Slide 330: FUNDAMENTALS: MAI
11
MAI (Cont’d)
  The power of MAI depends on two factors:
    the cross-correlation between different PN codes
    The signal power of interfering users
  Near-far effect
    Interfering users are close to BS (“near”)  high power at Rx
    Desired user is far away from BS (“far”)  low power at Rx
    the power of the interfering users is much higher than the power of the desired signal  MAI is high  signal to MAI ratio is low  poor performance of desired user
    Near-far effect will seriously affect the performance of CDMA system
    To reduce the impairments of near-far effect, the power at Rx should be the same for all users
– Close to BS: low Tx power. Far from BS: larger Tx power
    Power control is very important for CDMA system.

## Slide 331: FUNDAMENTALS: SPREAD SPRECTRUM
12
Bandwidth of CDMA signals
– TDMA or FDMA system: one symbol is transmitted at one symbol period (Ts)
Each symbol passes through pulse shaping filter with parameter
Bandwidth: BW  (1)Rs  (1) / Ts
– CDMA system: N chips are transmitted at one symbol period (Ts)
Modulation
Spreading
Pulse shaping
(,Ts )
each chip passes through pulse shaping filter with parameter (,Tc )
Bandwidth: BW  (1)Rc  (1) / Tc
Rc  NRs : chip rate
  The bandwidth is proportional to chip rate (N times of symbol rate)
The bandwidth of the signal is spreaded N times  spread spectrum!
  Within one symbol period, signals changes N times faster due to
spreading code.
Due to the properties of PN code, signals look like noise  high security

## Slide 332: FUNDAMENTALS: SPREAD SPRECTRUM
13
Bandwidth of CDMA signals (Cont’d)
– Pulse shaping
Time (Tc)
Chip period
Frequency (Rc)
 / 2
BW  (1 )Rc
Chip rate
bw  1 / Ts
BW  1 / TC
f
fc

## Slide 333: FUNDAMENTALS: SPREAD SPECTRUM
14
Bandwidth after despread
  After the operation of despread, each symbol period there is only one symbol  BW  1 / Ts
    The bandwidth of the original signal is recovered after despread.
bw  1 / Ts
BW  1 / TC
f
Before spread after spfc read
bw  1 / Ts
after despread
How about noise and signals from other users?
  Signals from other users: they use different codes  cross-correlation
is low  they remain to be wideband interference (MAI)
  Noise: noise inner product with PN code  noise properties remain the same.

## Slide 334: FUNDAMENTALS: PROCESSING GAIN
15
Processing gain
– Narrow band interference
f
signal
interference
fc
In channel
f
signal
interference
fc
After despread
At receiver, perform inner product between narrow band interference and PN code
  Equivalent to perform spreading operation over interference
Interference is spreaded, while signal is recovered !
  Interference: BW 1 / Tc
  Signal: BW  1 / Ts
  Most of the interference are removed!

## Slide 335: FUNDAMENTALS: PROCESSING GAIN
16
Process gain (Cont’d)
– Processing gain is an approximate measure of the interference rejection capability
 N
Rs Tc
 Ts
PG  Rc
Process gain is equal to the number of chips per code.
The higher the processing gain, the greater the ability to suppress narrow
band interference.

## Slide 336: FUNDAMENTALS: FHSS
17
Frequency-hopping spectrum
  A wide spectrum is divided into N sub-channels
  At each chip period, the carrier frequency of the signal is in one sub- channel
    At next chip period, the carrier frequency of the signal is in another sub-channel
    The signal “hops” from frequency to frequency
– The signal itself is still narrow band.
  At each symbol period, the signal hops N times
    The order of hopping is determined by the PN code.
  Very good security
    It‟s hard to guess which sub-channel the signal is at without the knowledge of the PN code
    Usually used in military applications.

## Slide 337: OUTLINE
18
CDMA Fundamentals
Pseudo-noise sequence
Rake receiver

## Slide 338: PSEUDO-NOISE SEQUENCE
19
PN sequence
  A binary sequence with an autocorrelation resembles the autocorrelation of white noise.
  Nearly equal number of 0s and 1s
  Low correlation between time shifted versions of the same sequence
  Very low cross-correlation between any two sequences.
Many methods exist for the generation of PN sequences
  Walsh code
  m-sequence
  Gold sequence
  ……

## Slide 339: PN SEQUENCE: WALSH CODE
20
Walsh code
C1  1
1 | 1
1 | 0
1 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
 i i 
 Ci Ci 
C
i1 C C 
Each row of the matrix is a PN sequence
The PN sequences generated by using Walsh code are perfectly orthogonal with each other.
Sequence length:
There are N length-N sequences.
N  2m

## Slide 340: PN SEQUENCE: M-SEQUENCE
21
m-sequence
(m: # of registers)
Also called maximal length sequence
Sequence length: N  2m1
Generated by using shift register
– E.g. m = 3 (N = 7)
a2 | a1 | a0 | s(n)
0 | 0 | 1 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
0 | 1 | 1 | 1
a2 = a1+a0
s(n) = a0
a2
a1
a0
1 0 0 1 0 1 1
Periodic with period N = 7
s(n)

## Slide 341: PN SEQUENCE: M-SEQUENCE
22
billions
The sequence will repeat itself for every 4398 billion chips
Long code
Can be used for scrambling (security)
  Different users start the sequence from different offsets.
  User data is XORed with chunks of long code with same length.
  Impossible to detect the data without knowledge of long code.
m-sequence (Cont’d)
– 15 registers: m = 15  N  215 1  32767
  The sequence will repeat itself for every 32767 chips.
  Short code
  Can be used for synchronization between Tx and Rx
– Only when the clock between Tx and Rx are synchronized will the receiver gets strong signal  adjust the receiver clock until a strong signal is obtained  synchronization.
– 42 registers: m = 42  N  242 1  4398

## Slide 342: PN SEQUENCE: IS-95 CDMA
23
Source
code
Convolutional
code
interleaver
Pulses
shaping
Pulses
shaping
long
code
Walsh
code
I-short
code
Q-short
code
c
cos(2f t)
c
sin( 2f t)
19.2kbps
1.2288 Mchips/s spreading
19.2kbps
scrambling
1.2288 Mchips/s
synchronization
upconversion
N  1.2288 M /19.2K  64

## Slide 343: OUTLINE
24
CDMA Fundamentals
Pseudo-noise sequence
Rake receiver

## Slide 344
25
RAKE RECEIVER
Rake receiver
Spread spectrum: signal bandwidth is very large  signal BW >> channel coherence BW  frequency selective fading
  Relative delay among multipath components is no longer negligible.
The received signal is the combination of signals with different delays.
E.g. two path equal gain channel, space between two channel taps: 4 chips
r  h0  sm cm  h1  sm cm (4)  n
Time shifted version of code
m
c
m
c (4)
0
h*
*
n1
0 1 m m m
0 m
2 s
c
 h h s   c (4) z
h
*
n2
1 m
2 s
m
1 0 m m
c  c (4) z
 h h s
h
1
h*
m
h 2 s
0
2
0
 h
interference
r

## Slide 345
26
RAKE RECEIVER
Rake receiver
  Rake receiver is made up of several Rake fingers
    Each finger corresponds to one of the multipath components.
  Due to the low correlation between time shifted version of the same PN code, each finger can be treated as flat fading  no equalization needed!
Delay
 0
Delay
1
Delay  L1
……
L1
h(t, )  hl (t)  ( l )
l 0

## Slide 346: CDMA
27
Major advantages:
  Resistant to narrow band interference
  Combats multipath fading (no equalization required)
  Multiple users can share the same spectrum
  Good security
Major disadvantages
  MAI
    Near-far effect.

## Slide 347: ELEG 5693 Wireless Communications Ch. 9 Wireless Netowrks
Department of Electrical Engineering
University of Arkansas
Dr. Jingxian Wu
wuj@uark.edu

## Slide 348: OUTLINE
2
Ad hoc wireless networks
Protocol layers
Cross-layer design

## Slide 349: AD HOC WIRELESS NETWORKS
Ad hoc wireless network
  A collection of wireless mobile nodes that self-configure to form a
network without the aid of any established infrastructure.
  Ad hoc: with little or no planning, fashioned from whatever is immediately available
  Different from: infrastructure-based network (such as cellular network)
  Allow people and devices to seamlessly internetwok in areas with no preexisting communication infrastructure.
    No pre-installed basestations
  Self-organizing, Rapidly deployed
    Nodes cooperate to provide connectivity  multihop relay.
    Easily enable instantaneous person-to-person, person-to-machine, or machine-to-person communications.
  Self-healing
    Even we one or some nodes break down, the network can still operate.
3

## Slide 350: AD HOC WIRELESS NETWORKS
Examples
  Ad-hoc mode of IEEE 802.11
    IEEE 802.11 (Wireless LAN) has two modes
      Infrastructure mode: wireless router, laptops
      Ad-hoc mode: no wireless router.
» Laptops can directly talk with one another without router.
  Mesh extension of IEEE 802.16
    Regular operation of IEEE 802.16 (WiMax) requires basestation.
    Mesh extension can provide services to users that do not have good coverage from BS.
      Signals are relayed from other users.
  Soldiers equipped with multimode mobile communication devices on battle field
    No fixed wireless base station or pre-installed infrastructrue are needed.
  Small vehicular devices equipped with sensors in hostile environment to collect data.
    Data are relayed by the sensor nodes.
  Ship-to-ship ad-hoc communication
    Doesn’t need the assistance from satellite.
  Police, rescue, etc.
4

## Slide 351: AD HOC WIRELESS NETWORKS
Evolution
  PRNET (packet radio network) : the first MANET
    Sponsored by DoD (Department of Defense), launchened in 1972
    Evolved into survivable adaptive radio networks (SURAN) in 1980s
    Goal: provide packet-switched networking to mobile battlefield elements in an infrastructureless, hostile environment.
    MAC layer: combination of ALOHA and CSMA (carrier sensing
multiple access)
    Network layer: a variation of distance vector routing.
    Handled datagram traffic reasonably well.
  Ad-hoc mode of IEEE 802.11: 1990s
  NTDR (Near-term digital radio): sponsored by DoD
    Used by U.S. Army in late 2002
    Clustering, link-state routing, self-organized two-tier structure.
  Still largely an R&D activity
    IETF MANET workgroup: two protocols will become “proposed standards”
5

## Slide 352: OUTLINE
6
Ad hoc wireless networks
Protocol layers
Cross-layer design

## Slide 353: INTRODUCTION: SOFTWARE AND PROTOCOLS
Network software is organized as a stack of layers
– Modular architecture makes development easier and cheaper

## Slide 354: INTRODUCTION: SOFTWARE AND PROTOCOLS
Layered structure: vertical
  Each layer provides services to the layers above
    Via the interface between layers.
    Details of the implementation of each layer is hidden to the higher layers  Data Encapsulation.
  Between each adjacent pair of layers is an interface
    Interface clearly defines the services the lower layer makes available to the upper layer.
    Clear cut interface make it simpler to change layer implementation 
different host can use different implementation.
  A layer in a machine is represented by an entity in that machine.
    Entity (SW or HW) does the function of that layer.

## Slide 355: INTRODUCTION: SOFTWARE AND PROTOCOLS
Layered structure: horizontal
  Peer Entities
    Entities in the same layer, but in different machines.
    Layer n on one machine carries on conversation (exchanges information) with layer n on another machine.
    Peer entities communicate with each other using protocol.
  Protocol: An agreement between communication parties on how
communication is to proceed.
    One of the most important concepts in computer network!
    Each layer has its own protocol.
    The protocol of a certain layer can only be understood by its peer entities.
  Physically, peer entities do not talk with each other directly.
    Using the layers below them until the physical medium.
    Actual communication occurs through physical medium

## Slide 356: INTRODUCTION: SOFTWARE AND PROTOCOLS
The philosopher–translator–secretary architecture
English
English Dutch
French
French Dutch
Peer Entities
Peer Entities
Peer Entities

## Slide 357: INTRODUCTION: SOFTWARE AND PROTOCOLS
Protocol Stack: A list of protocols used by a certain system, one protocol per layer.
Protocol Data Unit (PDU):
  A unit of data that is specified by a protocol of a given layer and delivered among peer entities.
  Consisting protocol control information of given layer and possibly data of that
layer.

## Slide 358: INTRODUCTION: SOFTWARE AND PROTOCOLS
Open System Interconnect (OSI) model
End-to-end layers
Chained layers

## Slide 359: Web, email, ftp, etc. TCP IP MAC
INTRODUCTION: SOFTWARE AND PROTOCOLS
A simplified model

## Slide 360: PHYSICAL LAYER
Physical layer is responsible for
  Transmitting information over the physical medium
    Make sure that when a ‘1’ is sent out at Tx, a ‘1’ is received at Rx.
  Activation and deactivation of physical connections.
Physical layer specifies interface characteristics
  Mechanical interface.
    E.g. number of pins of the connector, the shape of the connector, etc.
  Electrical interface.
    E.g. volts used to represent ‘1’, how long should a bit last, etc.
  Procedural interface.
    E.g. the sequence of events to activate/deactivate a physical medium.
Example physical layer standards
  RS-232, V.92, X.21

## Slide 361: PHYSICAL LAYER
Unguided transmission media
  Electromagnetic Waves
    Change of electrical field causes change of magnetic field, and vice versa
    Electromagnetic waves can propagate through space
15
Low
Medium
High
Very High
Ultra High
Super High
Extremely High
Tremendously High

## Slide 362: PHYSICAL LAYER
Spectrum Allocation
  Worldwide, ITU-R coordinates the allocation of spectrum
    One device can be used in multiple countries
  In U.S., FCC (Federal Communication Commission) is in charge of the spectrum allocation.
Spectrum Allocation Algorithms
  Beauty Contest: Each carrier explains why its proposal serves public best.
  Lottery: Lottery is held among interested companies
  Auctions: Certain bandwidth is given to the highest bidder.
ISM (Industrial, Scientific, Medical) bands
  Allocated by government for unlicensed use (device power must be under
1watt to avoid interference)
  Bluetooth, WiFi, cordless phone, etc.

## Slide 363: LINK LAYER
Link layer
  Deals with reliable communication between adjacent machines.
  The channel acts as a wire  no switching or routing
Functions of data link layer
  Providing well-defined service interface to the network layer
  Framing
    Encapsulates packets from network layer to frames.
  Flow control
    Keep fast transmitter from swamping slow receiver
  Dealing with transmission errors
    Error detection
    Error correction
  Media access control (MAC)
    Determine how to allocate a single broadcast channel (multi access
channel) among multiple competing users

## Slide 364: LINK LAYER
Services to upper layer
  The entity in data link layer is usually a software (might be embedded in a
chip)
  One router might have multiple different data link layers
    E.g. connecting both wireless network and wired network
(a) Virtual communication
(b) Actual communication

## Slide 365: LINK LAYER
Framing
  Encapsulate packet from network layer to frame
    Breaks down larger packets
    Add header and trailer
Break raw bit streams from physical layer into streams
  Process each stream individually

## Slide 366: LINK LAYER
Flow Control
  Keep high speed Tx from swamping low speed Rx
  Feedback-based flow control
    Rx sends back information giving it permission to send more data.
Error Control
  Acknowledgement (Ack)
    Positive Ack: Tx successful. Negative Ack: Tx unsuccessful.
    Timer used at Txno Ack before timer expired = negative Ack.
      If Ack is lost, Rx will have multiple copies of same frame
      Sequence # is used to ensure no duplication and loss.
  Error detection and correction code
    Cyclic redundancy check (CRC)

## Slide 367: LINK LAYER
Media access control (MAC)
  Determine how to allocate a single broadcast channel (multiaccess
channel) among multiple competing users
  Collision: Two devices transmit simultaneously, they overlap in time and collision occurs
MAC classifications
  Static channel allocation
    E.g. frequency division multiple access (FDMA): statically allocate a portion of the bandwidth to each user (broadcast TV)
    E.g. time division multiple access (TDMA): divide time into slots,
and allocate different slots to different users (cell phone systems)
  dynamic channel allocation
    Dynamically allocate channel to competing users.
    Efficient for bursty traffics: data coming in irregularly. – Most widely used in LANs

## Slide 368: LINK LAYER
MAC example: CSMA
Carrier sensing multiple access
Before sending out data, hosts listen to the carrier to see if there is transmission in the channel.
If there is transmission, host
will back off.
If there is no transmission, host will act differently for different CSMA protocols
Listens to channel
Wait for a random
Time.
Transmit
immediately
Collision?
Transmission
complete
Channel busy?
No
Yes
No
Yes
Nonpersistent

## Slide 369: NETWORK LAYER
resent.
23
Functions: getting packets from the source to the destination.
  Routing
    choose appropriate path for a packet; knowledge of the topology.
  Internetworking
    connect different types of networks (cooper, fiber optic, wireless, etc.).
  Quality of Service
  Congestion Control
    avoid overloading some of the lines.
  Service to transport layer
    Connectionless service
    Connection oriented service (virtual circuit service)
    Transport layer should be shielded from the number, type, and
topology of the routers p
Routers can be in either subnet
(owned by operator) or LAN (owned by end users).

## Slide 370: NETWORK LAYER
Routing
  Deciding which output line an incoming packet should be forwarded to.
  Datagram routing (connectionless):
    routing is performed for every packet.
    A packet is called a datagram
  Virtual circuit routing (connection oriented)
    routing is only performed at connection setup  session routing.
    All packets of the same session following the same route
Shortest path: find out the route with the shortest “distance” between source and destination.
  Different measures can be used to measure “distance”
    E.g. # of hops, physical distance (km), queuing delay …
  In practical system, the “distance” measure is usually a function of the distance, bandwidth, average traffic, communication cost, mean queue length, delay, and other factors.
24

## Slide 371: INTERNETWORK: CONNECTION
25
Internetworking: how networks can be connected
  Physical layer: repeater, Hub
  Data Link layer: switch, bridge
  Network layer: router (gateway: multi-protocol router)
  Transport layer: transport gateway
  Application layer: application gateway
Switch (the entire frame is transmitted)
Router (only IP packet is transmitted)

## Slide 372: INTERNETWORK: CONNECTIONLESS INTERNETWORK
26
Connectionless Internetwork
  Packets might go through different paths.
  Protocol translation.
  Address mapping
  IP packet is a “universal” packet recognized by most networks.

## Slide 373: NETWORK LAYER IN INTERNET
27
Internet Protocol (IP) is the glue for Internet
  IP was designed with internetworking in mind.
  It provides best-efforts (not guaranteed) way to transmit datagram from source to destination.

## Slide 374: INTERNET: IP PROTOCOL
28
Version: the version of the protocol (IPv4, IPv6)
IHL (4 bits): header length (in the unit of 32-bit word, or 4-byte word).
  Min value = 5  5 x 4 = 20 bytes. Max value = 15  15 x 4 = 60 bytes.
Type of service (6 bits): used to distinguish different service classes (QoS).
  Differentiated services: 4 queuing priorities, 3 discard probabilities, etc.
  This field has been ignored by routers.
Total length (16 bits): the total length of the IP packet (including header and data)
Maximum length:
216 = 65536 bytes = 64KB

## Slide 375: INTERNET: IP PROTOCOL
29
Identification (16 bits): identify which datagram a fragment belongs to.
  Fragments belonging to the same datagram has the same ID field.
DF: Don’t fragment.
MF: More fragment. More fragments are following.
  All fragments except the last one have this bit set to 1.
Fragment Offset (13 bits): the seq. # of the first elementary fragment in the current fragment. Elementary fragment: 8 bytes.
213
= 8192 elementary fragments.  8192 x 8 = 65536 bytes.
Time to live (8 bits): decrease by 1 after each hop.
  When hits 0, packet is discarded and a warning is sent back to source.
Protocol: which protocol is on the transport layer (TCP, UDP, etc.)
Header checksum: check header only. MUST be recomputed at each router! Why?
Source address (32 bits): IP address of source.
Destination address (32 bits): IP address of destination.

## Slide 376: INTERNET: IP PROTOCOL
30
Option: variable length. Can contain many options
  Each option starts with 1 byte word to identify the option
  Some options
More options can be found at www.iana.org/assignments/ip-parameters

## Slide 377: INTERNET: IP ADDRESS
IP address: 32-bit
  232 = 4295 million addresses.
  Format: dotted decimal.
    Binary: 11000000.00101001.00000110.00010100
    Hexadecimal: C0.29.06.14 – Hexadecimal:Binary
0: 0000; | 1: 0001; | 2: 0010; | 3: 0011
4: 0100; | 5: 0101; | 6: 0110; | 7: 0111
8: 1000; | 9: 1001; | A: 1010; | B: 1011
C: 1100; | D: 1101; | E: 1110; | F: 1111
Decimal: 192.41.6.20
– 12x16+0 = 192; 2 x 16+9=41; 0x16+6=6; 1x16+4=20.
– IP address assignment is managed by ICANN (Internet Corporation for
Assigned Names and Numbers)
31

## Slide 378: INTERNET: IP ADDRESS
32
IP addresses are divided into 5 classes
  0.0.0.0: this host
  255.255.255.255: broadcast
128 networks with 16 million hosts
16384 networks with 64K hosts.
2 million networks with 256
hosts.
Multicast
Reserved

## Slide 379: INTERNET: IP ADDRESS
33
Special IP addresses
Loopback: for testing only.
  Packets sent to this address will not be put in the wire.
  They are going to be processed locally as incoming packets.

## Slide 380: INTERNET: IP ADDRESS
34
Subnet
  Allow a single network be split into small parts for internal use but still act
like a single network to the outside.
    E.g. Each LAN within the network is a subnet.

## Slide 381: INTERNET: IP ADDRESS
35
Subnet (Cont’d)
  Some bits of the host number are used to identify subnet.
    E.g. in a class B network, 16-bits are used to identify hosts in the network. Among the 16-bit, 6 bits are used for subnet # (64 Ethernets), 10 bits are used for host # (1022 hosts in each subnet).
    Subnet mask: 11111111.11111111.11111100.00000000 (255.255.252.0, or
130.157.23.16.0/22)
– 22 bits are used for network # and subnet #; 10 bits are used for host #
  Router in the network can route packet based on the subnet #.
E.g: subnet 1: 100000010 00110010 000001|00 00000001
subnet 2: 100000010 00110010 000010|00 00000001
Each IP contains three fields: network address, subnet address, host address

## Slide 382: INTERNET: IP ADDRESS
36
NAT (Network Address Translation)
  Motivation: Most users want static IP address  We are running out of IP
addresses!
  Solution: Assign 1 or a few IP to company or ISP; Private IP are used inside company or ISP; NAT is used for address translation!
    Private IP address ranges
10.0.0.0 - 10.255.255.255/8 (16,777.216 hosts)
172.16.0.0 - 172.31.255.255/12 (1,048,576 hosts)
192.168.0.0 - 192.168.255.255/16 (65,536 hosts)
    Packets leaving local network will be replaced with true IP address.

## Slide 383: INTERNET: IP ADDRESS
37
NAT (Cont’d)
  All incoming packets are addressed to the real IP of the network.
    How to distinguish incoming packets for different hosts?
  TCP (or UDP) has header fields for source port and dest. port.
    Each port corresponding to one of the processes in host.
      E.g. port 80: http; port 21: ftp;
  NAT uses TCP source port to distinguish hosts!
    Each host is assigned a unique TCP port # at NAT.
    NAT maintains a table (host # and original port # v.s. NAT mapping
port #)
    When a packet is sent to NAT from the private network
      its IP address is replaced by real IP address;
      its TCP src port is changed to the NAT port based on ( host # and
original TCP port #).

## Slide 384: INTERNET: INTERNET CONTROL PROTOCOLS
Department of Engineering Science Sonoma State University
38
Address Resolution Protocol (ARP)
  How to find Ethernet address (MAC) by IP address?
  E1 to E2: Host 1 broadcasts an ARP packet asking: what is the MAC address for 192.31.65.5?
    Host 2 answers with its own MAC address.
    All the hosts make an entry in their own (IP, MAC) mapping table for host 1
and 2.
  E1 to E4: Host 1 sends the packet with dest. MAC address being F1 (or broadcast).
    F1 builds a new MAC frame to F3
    F3 builds a new MAC frame asking about the MAC address of E4

## Slide 385: INTERNET: INTERNET CONTROL PROTOCOLS
39
RARP (Reverse Address Resolution Protocol)
  A newly booted host broadcast its MAC address, and asking for IP address.
  RARP server replies with the IP by looking the MAC in its table.
  Router won’t forward MAC broadcast message (dest: all ‘1’s).
    Each network needs an RARP server.
BOOTP
  A newly booted host broadcast its MAC address using UDP messages
    UDP message can be forwarded by routers
  BOOTP server will reply with IP and other information
    E.g. the IP address of file server to download Operating System image.
  The MAC/IP mapping table must be configured by hand.

## Slide 386: INTERNET: INTERNET CONTROL PROTOCOLS
40
DHCP (Dynamic Host Configuration Protocol)
  A newly-booted host broadcasts a DHCP DISCOVER packet.
  Each LAN has a DHCP relay agent
    Forward the message to DHCP server through unicast.
    The DHCP server might not be reachable through broadcasting.
  DHCP server automatically assigns an IP address to the host.
  Leasing: IP is assigned for that host for a period of time.
    Host must renewal before expiration.

## Slide 387: INTERNET: OSPF
41
OSPF (Open Shortest Path First) – RFC 2328
  An interior gateway (multi-protocol router) routing protocol: routing inside an
independent network (autonomous system, or AS).
  AS is divided into areas: a network or a set of contiguous networks.
    Each AS has a backbone area connected to all other areas.
    Router connecting to two or more areas is part of backbone.
  Four types of routers:
    internal routers, area border router, backbone router, AS boundary router

## Slide 388: INTERNET: BGP
42
BGP (Border Gateway Protocol)
  An exterior gateway routing protocol: routing between ASes.
  The major difference from interior gateway routing: need to consider politics
    E.g. Do not use United States for traffic from British Columbia to Ontario; Traffic starting at IBM should not pass Microsoft; Transit traffic of only paid customers, etc.
  The rules are manually configured in BGP routers.
  BGP used an enhanced distance vector protocol
    Exchanging information with neighbors about cost to all destinations.

## Slide 389: INTERNET: IPV6
43
IPv6: the evolution of IP
  16 bytes of addresses: support effectively unlimited addresses.
2168  3.41038
    For the entire earth (water & land), allow 71023per square meter!
  Header is simplifier compared with IPv4
    Fixed length: 40 bytes
    Packets can be processed faster in router  lower delay, larger throughput.
  Better support of options
    Many required fields in IPv4 become options in IPv6
  Better security
  Better support of QoS.
  Not compatible with IPv4, but compatible with most other protocols
    TCP, UDP, ICMP, IGMP, OSPF, BGP, DNS

## Slide 390: INTERNET: IPV6 MAIN HEADER
44
Version: 6
Traffic class: different service classes for QoS
Flow label: the label of a particular connection. Routers can use this field
for QoS purpose. (e.g., this flow is delay sensitive).
  Each flow is designated by source, destination, and flow #.

## Slide 391: INTERNET: IPV6 MAIN HEADER
45
Main Header (Cont’d)
  Payload length: how many bytes following the 40-byte header
  Next header: which of the 6 optional header is following the main header.
    If no optional header, tells which transport protocol to pass the packet to.
  Hop limit: same as Time to live in IPv4.
  IPv6 address notation: eight groups of four hexadecimal digits 8000:0000:0000:0000:0123:4567:89AB:CDEF
    Can be simplified as
8000::123:4567:89AB:CDEF
      Consecutive zeros are replaced by ::
      Leading 0s are omitted.

## Slide 392: TRANSPORT LAYER
Functions: provide reliable, cost-effective data transport from source to destination.
  Independent of the physical network
  Independent of the network structure & topology
  The first true end-to-end layer
    Transport layer does not exist on routers.
    Transport layer on the source is directly talking with transport layer on the destination.
    On other layers, e.g. network layer, the conversation is usually between intermediate neighbors.

## Slide 393: TRANSPORT LAYER
Connection-oriented service
  Three phases:
    Connection establishment
    Data transfer
    Connection release
  Packets belonging to the same connection might take different routes!
    If the underlying network layer is connectionless.
  Example: TCP (Transport Control Protocol)
Connectionless service
  No connection required
  E.g. UDP (User Datagram protocol)
  Could be on top of connection-oriented network layer

## Slide 394: TRANSPORT LAYER: WHY TRANSPORT LAYER?
48
Network layer providing connectionless and connection oriented services as well.
  Why do we need another layer?
Network layer mainly resides on routers
  Routers are owned by operators
  Users have no control about the operation of the network layer.
  If something goes wrong in the network, the users could do nothing to
stop it.
We need an addition layer on top of network layer to improve the QoS.
  If error happens in network, simply set up another connection.
  Lost data can be detected and compensated by transport layer.
  Provide a unified interface to users
    Application programmers do not need to worry about the underlying network

## Slide 395: TRANSPORT LAYER: SERVICE PRIMITIVES
49
Service primitives
  A set of interfaces for the user to access the service
  Usually in the form of function calls.
  Analogy: printf( ) is the service primitive for the format printing service provided by C language.
    Users do not need to know the implementation of the function.
Different transport layer protocols have different service primitives

## Slide 396: TRANSPORT LAYER: SERVICE PRIMITIVES
50
The service primitives shield the underlying implementations from users
  Acknowledgement, lost packets, congestion, etc. are invisible to users.
  Provide reliable service on top of unreliable networks
  All users need to do is call SEND to send a packet at source, and call RECEIVE at destination to retrieve the packet.
Used directly by programmers or users
  Usually are convenient and easy to use.
A simple example

## Slide 397: TRANSPORT LAYER: BERKELEY SOCKETS
51
Berleley sockets
  Socket: access point for the service in transport layer.
  Servives primitives used in Berkeley Unix for TCP.
  Part of the OS kernel.
  The most widely used service primitives for TCP.
In Linux or Unix system, use man command_name (e.g. man socket) to get more information.

## Slide 398: TRANSPORT LAYER: UDP
52
User datagram protocol (UDP) – RFC 768
  Connectionless protocol
  Simple: IP with a short header
  Fewer message required (no connection setup, acknowledgement).
  Example: DNS (Domain Name System)
    Client send a request contains a domain name
    DNS server replies the IP of the domain name
    Only two messages.
  Good for short transaction, or delay sensitive applications.
Why UDP? Why not use IP directly?
  Each host has only one IP address
  Multiple network applications are running simultaneously.
  One UDP entity can provide services to multiple users.
    Each user has it’s own TCP port #.
  We can easily identify the destination application by using
    (IP, UDP port #)
We want to use the addressing element of UDP.

## Slide 399
53
UDP
Header
  Source port: port # of source
  Destination port: port # of destination
  Length: the length of the entire UDP packet (head + payload).
  Checksum: optional. All 0s if not computed.
What the UDP does not do
  Flow control
  Acknowledgement
  Retransmission (retransmission is meaningless for real-time application)
These operations are left to the applications!

## Slide 400: UDP: REAL-TIME TRANSPORT PROTOCOL
54
Real-time transport protocol (RTP)
  The engine for real-time applications
    Internet telephony, videoconferencing, video-on-demand, etc.

## Slide 401: TCP: SERVICES
55
Transmission control protocol – RFC 793, 1122, 1323
  Reliable end-to-end byte stream over an unreliable internetwork
    IP gives no guarantee of the delivery of datagram
    It’s up to TCP to guarantee the in-order and reliable delivery of the data to application layer.
TCP service model
  Application access the services provided by TCP by creating sockets at
both communication parties.
    Each socket is associated with a unique port number.
  Connections are established between sockets.
    One socket might be used for multiple connections.
– E.g. several users can connect to the same FTP server simultaneously.
  Byte stream: all bytes are treated equally.
  Full duplex: data transmissions can occur at both directions
simultaneously.

## Slide 402: TCP: SERVICES
56
Daemon
  Server programs runs at background
    FTP daemon is associated with port 21
  Internet daemon (inetd)
    Attached to multiple ports and waiting for connection requests.
    When a connection request for a particular application comes in, inetd will fork of a new process and wake up the corresponding service daemon.

## Slide 403: TCP: PROTOCOL
Source port, destination port
  16-bit:
  Specify the sockets on source and destination.
Sequence number:
  For a particular connection, each byte has its own sequence number
  The sequence number of the first byte in the payload
Acknowledge number: (Used in combination with the ACK flag)
  All bytes (0, Ack# - 1) have been successfully received
  The next expected byte is Ack#.

## Slide 404: TCP: PROTOCOL
TCP header length (in the unit of 32-bit word)
  How many 32-bit words are in the TCP header.
  Fixed header: 20 bytes. Optional header: variable length.
URG: urgent flag, used in combination with urgent flag
  If set to 1, indicating the urgent pointer is in use
Urgent pointer: (relative offset from the seq#)
  pointing to a byte in the payload starting from which the data is urgent
  TCP will be notified by application which data is urgent
– E.g. telnet, ctrl+C to terminate an application.
  If the data is urgent, TCP cannot hold it in buffer. Must deliver it immediately even if the sender window is 0.

## Slide 405: TCP: PROTOCOL
Ack: when set to 1, the Ack# is valid. Otherwise Ack# will be ignored.
PSH: PUSH flag
  When set to 1, notify TCP entity to send out data immediately.
  E.g. in remote login, hit enter.
RST:
  when set to 1, reset a connection (due to crash or other reasons).
  Also used to reject invalid TCP packets (e.g. delayed duplicate).
SYN: used for connection establishment
  Connection request: SYN = 1, ACK = 0.
  Connection accept: SYN = 1, ACK = 1.
CES440: Introduction
59
Jingxian Wu, 8/16/2005

## Slide 406: TCP: PROTOCOL
60
FIN: set to 1 used for connection release.
  After sending out a packet with FIN = 1, the host will no longer transmit more data. (but will continue receive data)
Window size: used for flow control

## Slide 407: TCP: PROTOCOL
61
Checksum
  checks TCP header, data, and part of the IP header (source IP, dest. IP,
protocol (6), TCP packet length)  violate the layered structure
  Other than TCP header, the following fields are checked.

## Slide 408: TCP: CONNECTION ESTABLISHMENT
62
Service primitives
  Server: LISTEN, ACCEPT
  Client: CONNECT
Three-way handshake
  After CONNECT is called, a connection request packet will be generated.
    Connection request packet (SYN = 1, ACK =0, Seq# = x).
    When the connection request packet arrives at the receiver, the receiver checks if LISTEN and ACCEPT have been executed for the port.
    If server accepts request, send back Ack (SYN = 1, ACK=1, Ack# = x+1, Seq# = y)
– Client sends back an Ack (SYN=0, ACK=1, Ack#=y+1) to finish the three way handshake.
    If server rejects request, send back Rej (RST = 1, ACK = 1, Ack#=x+1)
    The initial sequence# (x, y) are assigned based on the clock at the hosts.

## Slide 409: APPLICATION LAYER
63
The applications directly used by the end users
Examples
  HTTP (Hyper Text Transfer Protocol)
  FTP (File Transfer Protocol)
  E-mail

## Slide 410: PROTOCOL: MAJOR CHALLENGES
64
Major challenges
  Network layer: dynamic routing
    Nodes are mobile
    Distributed multihop wireless network with time-varying topology.
  MAC sublayer:
    Hidden station problem
    Exposed station problem
  Physical layer
    Power consumption.
    Unreliable wireless link

## Slide 411: OUTLINE
65
Ad hoc wireless networks
Protocol layers
Cross-layer design

## Slide 412: CROSS-LAYER DESIGN
Cross-layer design
  Perform joint optimization across protocol layers
  Why?
    Layered structure works well for conventional wired networks
    The isolation of layers doesn’t work very well for wireless ad hoc network
      Can’t perform optimization across layers
      The physical channel and the network structure is constantly changing  the layered structure might not be able to respond to the change fast enough
66

## Slide 413: CROSS-LAYER DESIGN
Example 1
  Physical layer: adaptive modulation and coding (AMC)
    Select the modulation and coding based on the channel condition
  Network layer:
    Adaptive routing: there might be multiple paths between source and destination. Select the path with the better physical layer performance.
Example 2
  Hybrid Automatic Retransmit Request (HARQ)
    In the MAC layer, if there is collision during transmission, re-transmit
    Perform maximal ratio combining (MRC) between the originally
transmitted signal and the re-tx signal at the physical layer.
Example 3
  Cooperative diversity: multiple spatially distributed nodes to help the
forward of a node
  Network diversity: multiple routes through the network are used to send a single packet
67